## Slide 1: Maestro: Orchestrating Predictive Resource Management in Future Multicore Systems
Sangyeun Cho, Socrates Demetriades
Computer Science Department
University of Pittsburgh

## Slide 2: Prelude
Heterogeneity in multicore processors will grow
1. Designers adopt asymmetry
[Kumar et al., ’03]
large, fast, high power
small, slower, low power

## Slide 3: Prelude
Heterogeneity in multicore processors will grow
2. Processor variations render processor cores “unintentionally” different
[Borkar, ’04]
core 0
core 1
core 2
core 3
fast, high power
slow, low power

## Slide 4: Prelude
Heterogeneity in multicore processors will grow
3. Imperfect resource management results in unbalanced and unfair resource usages
core 0
core 1
[Iyer, ’04]
shared cache

## Slide 5: Prelude
Heterogeneity in multicore processors will grow
4. Intermittent and permanent faults degrade a system
core 0
core 1
[Borkar, ’04]

## Slide 6: Our contributions
Observation
  Heterogeneity in computing resource grows
  Need to manage resources differently
Maestro: a system design framework
  To better deal with heterogeneous resources in multicore chips; to better scale them
Case study
  Parallel program is split into “epochs”
  Remember how each epoch behaved
  Utilize past behavior to predict and control future

## Slide 7: Deal with or not?
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.1835
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.35
Avg. Program Performance
(relative to RND)
σ/μ=0.08
σ/μ=0.16
(When offered load is low)
core 0
core 1
core 2
core 3

## Slide 8: Deal with or not?
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.1835
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.35
Avg. Program Performance
(relative to RND)
σ/μ=0.08
σ/μ=0.16
(When offered load is low)
core 0
core 1
core 2
core 3
3%
3%

## Slide 9: Deal with or not?
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.1835
Chart: 
| RND | BAL | Aware
 | 1 | 1.03 | 1.35
Avg. Program Performance
(relative to RND)
σ/μ=0.08
σ/μ=0.16
(When offered load is low)
core 0
core 1
core 2
core 3
3%
3%
18%
35%

## Slide 10
Awareness is key…
Two types of awareness:
execution environment; and
application behavior
Most systems, however, are NOT aware of heterogeneity (except NUMA)!

## Slide 11: Maestro: Vision
Learn environment automatically and annotate it
Learn application automatically and annotate it
System does better and better in matching an application with resources
There are many “how”s we need to study
  The paper lists many research questions

## Slide 12: Maestro: Big picture
execution environment
w/ asymmetric resources
…
…
applications
???

## Slide 13: Maestro: Learning environment
…
…
microbench
“environment profiler”

## Slide 14: Maestro: Learning application
…
…
program run
“application profiler”

## Slide 15: Maestro: Leveraging annotations
program run
…
…
“resource manager”

## Slide 16: Example problems
Initial task mapping
  Map a new task to a processor that fits the best at the time of mapping (c.f., random, round-robin, shortest queue, …)
Last-level cache management
  Allocate cache capacity based on prediction
Power and energy management
  Select a low-power core to minimize energy while meeting QoS

## Slide 17: Research questions
What parameters do we study? Dependency between resource parameters?
Which resource to characterize? How to represent? Microbenchmark?
Which level do we characterize an application? Program? Phase? Instruction? How?
What architectural support will enable effective and efficient learning?
See paper for details

## Slide 18: Cadenza: Case study
Purpose
  Prove the concept of predictive resource management
Goal
  Evaluate “epoch”-based performance-energy adaptation of on-chip network
Adaptation mechanism
  All-router DVFS (dynamic voltage-frequency scaling)

## Slide 19: Case study: Program epochs
Time
NoC Traffic
epoch “A”
epoch “B”
…
…
[Demetriades and Cho, ’11]

## Slide 20: Case study: Methodology
Benchmark
  PARSEC and SPLASH-2 (pthread)
Simulation setting
  Simics (full-system simulator) + cycle-accurate memory hierarchy module
  16 2-issue in-order cores
  Distributed shared L2 cache
  2D mesh NoC, x-y routing
  2-stage router pipeline, 2-entry buffer per VC

## Slide 21: Case study: Power model
Power consumption
  NoC power + others (background)
NoC power: DVFS
Frequency (GHz) | Voltage (V) | alias
3 | 0.8 | f100%
2.25 | 0.65 | f75%
1.5 | 0.5 | f50%
0.75 | 0.35 | f25%

## Slide 22: Case study: Evaluation space
Schemes with fixed NoC frequency
  f100% (baseline), f75%, f50%, f25%
Epoch-based DVFS (adaptive strategies)
  fDVFS-dyn: Run-time adaptation
  fDVFS-static: Statically (off-line) determined adaptation
Best frequency: one that minimizes the energy-delay product

## Slide 23: Case study: Results
Chart: % Energy Savings
| bodytrack | streamcluster | barnes | average
f-75% | 5.74 | 13 | 5.8992 | 7.2856
f-50% | 8.9206 | 7 | -49.4705 | 2.2702
f-25% | -35.7623 | -62 | -41.3225 | -38.4531
f-DVFS dyn | 15 | 16 | 3.4 | 12.4551
f-DVFS stat | 19.6832 | 23 | 3.466 | 16.549
Chart: % Slowdown
| bodytrack | streamcluster | barnes | average
f-75% | 7.3065 | 4 | 7.1253 | 6.1668
f-50% | 13.7382 | 20 | 86.6558 | 22.6093
f-25% | 79.6298 | 114 | 86.9866 | 83.1469
f-DVFS dyn | 7 | 2 | 3.1 | 3.3169
f-DVFS stat | 5.9844 | 1 | 3.0147 | 2.6898
Notes: Changing the frequency level of the NoC affects both energy consumption and performance.
Lower frequency at the NoC will save power but will slow down the network, potentially affecting the overall system performance.
The graph on the left will show the overall on-chip energy savings achieved by each scheme and the graph on the right the corresponding slowdowns, for the refer applications.
All the results will be shown with respect to the baseline scheme, where the NoC operates at full frequency f100%.

## Slide 24: Case study: Results
Chart: % Energy Savings
| bodytrack | streamcluster | barnes | average
f-75% | 5.74 | 13 | 5.8992 | 7.2856
f-50% | 8.9206 | 7 | -49.4705 | 2.2702
f-25% | -35.7623 | -62 | -41.3225 | -38.4531
f-DVFS dyn | 15 | 16 | 3.4 | 12.4551
f-DVFS stat | 19.6832 | 23 | 3.466 | 16.549
Chart: % Slowdown
| bodytrack | streamcluster | barnes | average
f-75% | 7.3065 | 4 | 7.1253 | 6.1668
f-50% | 13.7382 | 20 | 86.6558 | 22.6093
f-25% | 79.6298 | 114 | 86.9866 | 83.1469
f-DVFS dyn | 7 | 2 | 3.1 | 3.3169
f-DVFS stat | 5.9844 | 1 | 3.0147 | 2.6898

## Slide 25: Case study: Results
Chart: % Energy Savings
| bodytrack | streamcluster | barnes | average
f-75% | 5.74 | 13 | 5.8992 | 7.2856
f-50% | 8.9206 | 7 | -49.4705 | 2.2702
f-25% | -35.7623 | -62 | -41.3225 | -38.4531
f-DVFS dyn | 15 | 16 | 3.4 | 12.4551
f-DVFS stat | 19.6832 | 23 | 3.466 | 16.549
Chart: % Slowdown
| bodytrack | streamcluster | barnes | average
f-75% | 7.3065 | 4 | 7.1253 | 6.1668
f-50% | 13.7382 | 20 | 86.6558 | 22.6093
f-25% | 79.6298 | 114 | 86.9866 | 83.1469
f-DVFS dyn | 7 | 2 | 3.1 | 3.3169
f-DVFS stat | 5.9844 | 1 | 3.0147 | 2.6898
Notes: Reducing more the frequency of the NoC will reduce more the power consumption in the NoC.
However, the overall system-wide energy savings do not show much improvement here.
In fact most of the applications show that energy savings are worsed compared with the previous case of f75%.
This is caused by the large slowdowns seen by the application, as you can see on the right graph.
The time the application needs to complete is large enough to adverse the power reductions in the NoC to less overall energy savings.

## Slide 26: Case study: Results
Chart: % Energy Savings
| bodytrack | streamcluster | barnes | average
f-75% | 5.74 | 13 | 5.8992 | 7.2856
f-50% | 8.9206 | 7 | -49.4705 | 2.2702
f-25% | -35.7623 | -62 | -41.3225 | -38.4531
f-DVFS dyn | 15 | 16 | 3.4 | 12.4551
f-DVFS stat | 19.6832 | 23 | 3.466 | 16.549
Chart: % Slowdown
| bodytrack | streamcluster | barnes | average
f-75% | 7.3065 | 4 | 7.1253 | 6.1668
f-50% | 13.7382 | 20 | 86.6558 | 22.6093
f-25% | 79.6298 | 114 | 86.9866 | 83.1469
f-DVFS dyn | 7 | 2 | 3.1 | 3.3169
f-DVFS stat | 5.9844 | 1 | 3.0147 | 2.6898
-38.5
-83.2
Notes: This is exagerated when we reduce further the frequency, for example at f25%.
Here, all applications have very large slowdowns that eventually cause significan energy loss.

## Slide 27: Case study: Results
Chart: % Energy Savings
| bodytrack | streamcluster | barnes | average
f-75% | 5.74 | 13 | 5.8992 | 7.2856
f-50% | 8.9206 | 7 | -49.4705 | 2.2702
f-25% | -35.7623 | -62 | -41.3225 | -38.4531
f-DVFS dyn | 15 | 16 | 3.4 | 12.4551
f-DVFS stat | 19.6832 | 23 | 3.466 | 16.549
Chart: % Slowdown
| bodytrack | streamcluster | barnes | average
f-75% | 7.3065 | 4 | 7.1253 | 6.1668
f-50% | 13.7382 | 20 | 86.6558 | 22.6093
f-25% | 79.6298 | 114 | 86.9866 | 83.1469
f-DVFS dyn | 7 | 2 | 3.1 | 3.3169
f-DVFS stat | 5.9844 | 1 | 3.0147 | 2.6898
-38.5
-83.2
Run-time epoch-based DVFS shows 12.5% energy savings for 2.7% slowdown

## Slide 28: Case study: Results
Chart: ED Improvement
| bodytrack | fluidanimate | streamcluster | barnes | fmm | ocenan | radiosity | water-ns | average
f-75% | 0.98866 | 0.9367 | 1.1052 | 0.99201 | 0.98914 | 1.0917 | 0.95336 | 1.0945 | 1.0189
f-50% | 0.96532 | 0.91072 | 0.89606 | 0.35843 | 0.94703 | 1.162 | 0.84608 | 1.1757 | 0.90767
f-25% | 0.41006 | 0.27837 | 0.28845 | 0.37842 | 0.36265 | 0.85965 | 0.26504 | 0.80709 | 0.45621
f-DVFS dyn | 1.0995 | 1.1923 | 1.1671 | 1.0041 | 1.0477 | 1.1951 | 1.0031 | 1.184 | 1.1116
f-DVFS stat | 1.1748 | 1.3072 | 1.2858 | 1.0056 | 1.1052 | 1.2732 | 1.0207 | 1.2545 | 1.1784
Epoch-based strategies are robust and outperform all static schemes…
Notes: In all cases, both epoch-based dynamic schemes outperform the static schemes.
The run-time epoch adaptive scheme follows closely and consistently the off-line based scheme,
indicating the strength of the runt-time barrier watch approach in capturing correctly the changes in program behavior.
Also, a side-result here shows that operating the NoC at 75% of full frequency is on average a better ED choice than having the NoC running at full frequency.
Lastly, there are cases where epoch-based adaptation has no room for significant improvements.

## Slide 29: Postlude
We predict and examine the impact of growing heterogeneity in processor resources
We propose Maestro, a hypothetical system design framework to tackle heterogeneity with little manual intervention
  We envision a system that perform better and better over time
Our detailed case study reveals that learning an application can pay off

## Slide 30: Maestro: Orchestrating Predictive Resource Management in Future Multicore Systems
Sangyeun Cho, Socrates Demetriades
Computer Science Department
University of Pittsburgh