## Slide 1
* Memory Solutions Lab. (MSL)
Memory Division, Samsung Electronics Co.
Computer Science Department
University of Pittsburgh
Active Disk Meets Flash:
A Case for Intelligent SSDs
Sangyeun Cho*, Chanik Park, Hyunok Oh, Sungchan Kim, Youngmin Yi, Greg Ganger

## Slide 2: Data processing, a bird’s eye view
All data move from hard disk (HDD) to memory (DRAM)
All data move from DRAM to $$
Processing begins

## Slide 3: Active disk
“Execute application codes on disks!”
  [Riedel, VLDB ’98]
  [Acharya, ASPLOS ’98]
  [Keeton, SIGMOD Record ’98]
Advantages [Riedel, thesis ’99]
  Parallel processing – lots of spindles
  Bandwidth reduction – filtering operations common
  Scheduling – better locality
(Some) apps have desirable properties
  That can exploit active disks

## Slide 4: Why do we not have active disks?
HDD vendors driven by standardized products in mass markets
  Chip vendors design affordable & generic chips for wider acceptance and longevity
System integration barriers
  New features at added cost may not be used by many and convincing system vendors to implement support is hard
Independent advances like distributed storage
  Distributed storage is similar to active disk

## Slide 5: Active disk meets flash
Flash solid-state drives (SSDs) are on the rise
  “World-wide SSD shipments to increase at a CAGR of 51.5% from 2010 to 2015” (IDC, 2012)
  SSD architectures completely different than HDDs
We believe the active disk concept makes more sense on SSDs
  Exponential increase in bandwidth!
  Fast design cycles (Moore’s Law, Hwang’s Law)
We make a case for Intelligent SSD (iSSD)
  Design trade-offs are very different

## Slide 6: iSSD
Taps the SSD’s increasing internal bandwidth
  Bandwidth growth ~ NAND interface speed × # buses
  SSD-internal bandwidth exceeds the interface bandwidth
Incorporates power-efficient processors
  Opportunities to design new controller chips  SSD generation gap pretty short!
  Leverage parallelism within a SSD
Leverages new distributed programming frameworks like Map-Reduce

## Slide 7: Talk roadmap
Background
  Technology trends
  Workload
iSSD architecture
Programming iSSDs
Performance modeling and evaluation
Conclusions

## Slide 8: Background: technology trends
HDD bandwidth growth lags seriously
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015

 | 130 | 130 | 130 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
 | 0 | 3.8 | 7.6 | 7.6 | 7.6 | 15.2 | 15.2 | 15.2 | 30.4 | 30.4 | 30.4
CPU
Bandwidth (MB/s)
CPU throughput (GHz × cores)
HDD
Year

## Slide 9: Background: technology trends
SSD bandwidth ~ NAND speed × # buses
Host interface follows SSD bandwidth
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015

 | 68 | 108 | 108 | 133 | 133 | 133 | 400 | 400 | 800 | 800 | 800
 | 272 | 432 | 864 | 1064 | 2128 | 2128 | 9600 | 9600 | 19200 | 19200 | 19200
 | 130 | 130 | 130 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
 | 100 | 133 | 150 | 150 | 150 | 300 | 600 | 2000 | 4000 | 8000 | 8000
 | 0 | 3.8 | 7.6 | 7.6 | 7.6 | 15.2 | 15.2 | 15.2 | 30.4 | 30.4 | 30.4
CPU
Bandwidth (MB/s)
CPU throughput (GHz × cores)
HDD
SSD
NAND flash
Host i/f
24 ch.
16 ch.
8 ch.
4 ch.
Year

## Slide 10: Background: performance metrics
Program-centric (conventional)
  TIME = IC × CPI × CCT
  IC = “instruction count”, CPI = “clocks per instruction”, CCT = “clock cycle time”
Data-centric
  TIME = DC × CPB × CCT
  DC = “data count”, CPB = “clocks per byte”
  CPB = IPB × CPI

## Slide 11: Background: workload
Name | Description | Input
word_count | Counts # of unique word occurrences | 105MB
linear_regression | Applies linear regression best-fit over data points | 542MB
histogram | Computes RGB histogram of an image | 1,406MB
string_match | Pattern matches a set of strings against data streams | 542MB
ScalParC | Decision tree classification | 1,161MB
k-means | Mean-based data partitioning method | 240MB
HOP | Density-based grouping method | 60MB
Naïve Bayesian | Statistical classifier based on class conditional independence | 126MB
grep (v2.6.3) | Searches for a pattern in a file | 1,500MB
scan (PostgreSQL) | Finds records meeting given conditions from a database table | 1,280MB

## Slide 12: Background: workload
Chart: 
| word_count | linear_regression | histogram | string_match | ScalParC | k-means | HOP | Naïve Bayesian | grep | scan
CPB | 90 | 31.5 | 62.4 | 46.4 | 83.1 | 117 | 48.6 | 49.3 | 5.7 | 3.1
CPB
Chart: 
 | 87.1 | 40.2 | 37.4 | 54 | 133.7 | 117.1 | 41.2 | 83.6 | 4.6 | 3.9
IPB
Chart: 
 | 1.0333 | 0.8 | 1.7 | 0.9 | 0.6 | 1 | 1.2 | 0.6 | 1.2 | 0.8
CPI
CPB = Cycles Per Byte
IPB = Instrs Per Byte
CPI = Cycles Per Instr
CPB = IPB×CPI!

## Slide 13: iSSD architecture
…
…
Flash Channel #0
Flash Channel #(nch–1)
NAND Flash Array
…
Host Interface Controller
DRAM
Controller
DRAM
Host
On-Chip
SRAM
On-Chip
SRAM
…
Flash
Memory
Controller
ECC
Flash
Memory
Controller
ECC
CPU(s)
CPUs
Bus
Bridge
DMA
Scratchpad
SRAM
Flash
Interface
Embedded
Processor
Stream
Processor
…
R0,0
RN-1,1
…
R0,0
…
ALU0
ALUN-1
R0,1
zero0
zeroN-1
zero
result
ALU0
enable
…
…
ALU0
ALUN-1
…
R0,0
RN-1,1
RN-1,0
…
ALU0
ALUN-1
RN-1,1
zero
result
ALUN-1
…
ALU0
ALUN-1
enable
Main
Controller
Config.
Memory
Scratchpad SRAM Interface

## Slide 14: Why stream processor?
Imagine flash memory runs at 400MHz (i.e., 400MB/s bandwidth @8-bit interface)
Imagine an embedded processor runs at 400MHz
  If your IPB = 50; even if your CPI is as low as 0.5, your CPB is 25  25× speed-down!
Stream processing per bus is valuable
  Increases the overall data processing throughput
  Reduces CPB with reconfigurable parallel processing inside SSD

## Slide 15: Instantiating stream processor
CPB improvement of examples:
  3.4× (linear_regression), 4.9× (k-means) and 1.4× (string_match)
for each stream input a
for each cluster centroid k
if (a.x-xk)^2 + (a.y-yk)^2 < min
min = (a.x-xk)^2 + (a.y-yk)^2;
sub
mul
a.x
sub
mul
add
min
add
add
0
0
zero
x1,…,xk
a.y
y1,…,yk
x1,…,xk
y1,…,yk
enable
enable
(k-means)

## Slide 16: How to program iSSD?
Extensively studied
  E.g., [Acharya, ASPLOS ’98], [Huston, FAST ’04]
We use Map-Reduce as the framework for iSSDs
  Initiator: Host-side service
  Agent: SSD-side service
MapReduce Runtime
(Initiator/Agent)
1
Mapper
Mapper
Mapper
Mapper
Reducer
Reducer
Input
data
Map
Phase
Interme-
diate data
Reduce
Phase
Output
data
Embedded
CPU
DRAM
Flash
FMC
Flash
MapReduce
Smart SSD
1
File A
File B
File C
FTL
MapReduce Runtime (Agent)
Device driver
MapReduce Runtime (Initiator)
Applications
(Database, Mining, Search)
File System
Host interface
Application initializes the parameters
(i.e., registering Map/Reduce functions
and reconfiguring stream processors)
2. Application writes data into iSSD
Application sends metadata to iSSD
(i.e., data layout information)
Application is executed
(i.e., the Map and Reduce phases)
5. Application obtains the result

## Slide 17: Data processing strategies
Pipelining
  Use front-line resources in SSD (e.g., FMC, embedded CPU) before host CPU
  Filter/drop data in each tier
Partitioning
  If SSD takes all data processing, host CPUs are idle!
  Host CPUs could perform other tasks or save power
  Or, for maximum throughput, partition the job between SSD and host CPUs
We can employ both strategies together!

## Slide 18: Performance of pipelining
D: input data volume (assumed to be large)
B: bandwidth (1/CPB)
Steps (t*)
  Data transfer from NAND flash to FMC
  Data processing at FMC
  Data transfer from FMC to DRAM
  Data processing with on-SSD CPUs
  Data transfer from DRAM to host
  Data processing with host CPUs
Ttotal = serial time + max(t*), B = D / Ttotal

## Slide 19: Performance of partitioning
Input D is split into Dssd and Dhost
  Dssd is processed within SSD and Dhost is transferred from SSD to host for processing
  Host interface is not bottleneck if Dhost is small
Ttotal = max(Dssd/Bssd, Dhost/Bhost)
  Bhost can be put: nhost_cpu×fhost_cpu/CPBhost_cpu

## Slide 20: Also in the paper…
Validation of performance models
Prototyping results using commercial SSDs
Detailed energy models for pipelining and partitioning
1 2 4 8 16
model
sim
sim (XL)
model (XL)
k-means
1 2 4 8 16
model (XL)
sim
model
sim (XL)
linear_regression
Chart: 
 | 4294190.76 | 2147095.38 | 1073547.69 | 536773.845 | 268386.9225
 | 4294257 | 2184979 | 1087826 | 573746 | 293236
 | 3133812.3745 | 1566903.97 | 783451.985 | 391725.9925 | 195862.9962
 | 3060647.4877 | 1561101.7193 | 776758.7542 | 412637.956 | 211493.0248
0
1 2 4 8 16
sim
model
model (XL)
sim (XL)
string_match
Cycles
# flash channels
Chart: 
 | 3525300 | 1762650 | 881325 | 440662.5 | 220331.25
 | 3525302 | 1729302 | 847779 | 411192 | 243528
 | 777600 | 388800 | 194400 | 97200 | 48600
 | 727562.8535 | 357267.6919 | 175338.4027 | 85189.1225 | 50003.4488
Chart: 
 | 3956805.86 | 1978402.93 | 989201.465 | 494600.7325 | 247300.3663
 | 3956871 | 1994346 | 992722 | 525891 | 265890
 | 1357338.169 | 678669.0845 | 339334.5422 | 169667.2711 | 84833.6356
 | 1357348 | 694584.5 | 342841.25 | 200950.625 | 103419.8125
0
0

## Slide 21: Studied model parameters

## Slide 22: Performance (= throughput)
For linear_regression and string_match, host CPU performance (8 cores) is the bottleneck
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
host, 8GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
Data processing rate (MB/s)
Number of FMCs
HOST-SATA
HOST-4/8G
linear_regression
string_match
Number of FMCs
HOST-*
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
host, 4GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 8GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
Data processing rate (MB/s)

## Slide 23: Performance (= throughput)
Utilizing a simple embedded processor per channel in SSD is insufficient for these two programs
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 95.38 | 190.7601 | 286.1401 | 381.5201 | 476.9001 | 572.2802 | 667.6602 | 763.0402
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
host, 8GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
Data processing rate (MB/s)
Number of FMCs
ISSD-400.
HOST-SATA
HOST-4/8G
linear regression
string_match
Number of FMCs
ISSD-400
HOST-*
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 82.4317 | 164.8635 | 247.2952 | 329.7269 | 412.1587 | 494.5904 | 577.0222 | 659.4539
host, 0.6GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 4GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 8GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
Data processing rate (MB/s)

## Slide 24: Performance (= throughput)
“Acceleration” with stream processor (ISSD-XL) is shown to be effective, more for linear_reg.
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 95.38 | 190.7601 | 286.1401 | 381.5201 | 476.9001 | 572.2802 | 667.6602 | 763.0402
ISSD w/ acc | 318.408 | 636.8159 | 955.2239 | 1273.6318 | 1592.0398 | 1910.4478 | 2228.8557 | 2547.2637
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
host, 8GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
Data processing rate (MB/s)
Number of FMCs
ISSD-XL
ISSD-400.
HOST-SATA
HOST-4/8G
linear regression
string_match
Number of FMCs
ISSD-400
HOST-*
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 82.4317 | 164.8635 | 247.2952 | 329.7269 | 412.1587 | 494.5904 | 577.0222 | 659.4539
ISSD w/ acc | 112.9545 | 225.9089 | 338.8634 | 451.8179 | 564.7723 | 677.7268 | 790.6813 | 903.6357
host, 0.6GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 4GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 8GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
ISSD-XL
Data processing rate (MB/s)

## Slide 25: Performance (= throughput)
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 95.38 | 190.7601 | 286.1401 | 381.5201 | 476.9001 | 572.2802 | 667.6602 | 763.0402
ISSD w/ acc | 318.408 | 636.8159 | 955.2239 | 1273.6318 | 1592.0398 | 1910.4478 | 2228.8557 | 2547.2637
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
host, 8GB/s | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565 | 812.9565
ISSD 800MHz | 190.7601 | 381.5201 | 572.2802 | 763.0402 | 953.8003 | 1144.5604 | 1335.3204 | 1526.0805
Data processing rate (MB/s)
Number of FMCs
ISSD-XL
ISSD-400.
ISSD-800
HOST-SATA
HOST-4/8G
linear regression
string_match
Number of FMCs
ISSD-800
ISSD-400
HOST-*
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 82.4317 | 164.8635 | 247.2952 | 329.7269 | 412.1587 | 494.5904 | 577.0222 | 659.4539
ISSD w/ acc | 112.9545 | 225.9089 | 338.8634 | 451.8179 | 564.7723 | 677.7268 | 790.6813 | 903.6357
host, 0.6GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 4GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
host, 8GB/s | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053 | 551.6053
ISSD 800MHz | 164.8635 | 329.7269 | 494.5904 | 659.4539 | 824.3174 | 989.1808 | 1154.0443 | 1318.9078
ISSD-XL
Data processing rate (MB/s)
Circuit-level speedup (ISSD-800) is better than ISSD-XL for string_match
  There may be opt. opportunities for string_match

## Slide 26: Performance (= throughput)
k-means: host CPU limited
scan: host interface bandwidth limited
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
host, 0.6GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
host, 4GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
host, 8GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 3200 | 4096 | 4096 | 4096 | 4096 | 4096 | 4096 | 4096
host, 8GB/s | 3200 | 6400 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192
HOST-8G
HOST-SATA
HOST-4G
k-means
scan
Number of FMCs
Number of FMCs
HOST-*
Data processing rate (MB/s)
Data processing rate (MB/s)

## Slide 27: Performance (= throughput)
Both programs benefit from stream processor
Smart SSD approach is very effective for scan because of SSD’s very high int. bandwidth
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 20.3059 | 40.6117 | 60.9176 | 81.2234 | 101.5293 | 121.8351 | 142.141 | 162.4469
ISSD w/ acc | 98.735 | 197.4699 | 296.2049 | 394.9398 | 493.6748 | 592.4098 | 691.1447 | 789.8797
host, 0.6GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
host, 4GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
host, 8GB/s | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913 | 218.6913
ISSD 800MHz | 40.6117 | 81.2234 | 121.8351 | 162.4469 | 203.0586 | 243.6703 | 284.282 | 324.8937
Chart: 
| 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64
ISSD w/o acc | 800 | 1600 | 2400 | 3200 | 4000 | 4800 | 5600 | 6400
ISSD w/ acc | 3200 | 6400 | 9600 | 12800 | 16000 | 19200 | 19200 | 19200
host, 0.6GB/s | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4 | 614.4
host, 4GB/s | 3200 | 4096 | 4096 | 4096 | 4096 | 4096 | 4096 | 4096
host, 8GB/s | 3200 | 6400 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192
ISSD 800MHz | 1600 | 3200 | 4800 | 6400 | 8000 | 9600 | 11200 | 12800
HOST-8G
HOST-SATA
HOST-4G
k-means
scan
Number of FMCs
Number of FMCs
ISSD-XL
ISSD-XL
ISSD-800
ISSD-400.
ISSD-800
ISSD-400.
HOST-*
Data processing rate (MB/s)
Data processing rate (MB/s)

## Slide 28: Iso-performance curves
Measures when a Smart SSD performs better than host CPUs
Chart: 
| 4 | 8 | 12 | 16
linear | 34 | 51.5 | 51.5 | 51.5
string | 27 | 54 | 60 | 60
k-means | 43 | 86.3 | 129 | 172
scan | 6.1 | 6.1 | 6.1 | 6.1
Number of host CPUs
Number of FMCs
rhost = 600 MB/s
linear_regression
scan
k-means
string_match
Raw performance
4 host CPUs =
64 FMCs

## Slide 29: Iso-performance curves
Acceleration with stream processor improves the effectiveness of the iSSD
Chart: 
| 4 | 8 | 12 | 16
linear | 34 | 51.5 | 51.5 | 51.5
string | 27 | 54 | 60 | 60
k-means | 43 | 86.3 | 129 | 172
scan | 6.1 | 6.1 | 6.1 | 6.1
linear-acc | 10.2 | 15.4 | 15.4 | 15.4
string-acc | 19.5 | 39 | 43.5 | 43.5
k-means-acc | 8.8 | 18 | 26.6 | 35.4
scan-acc | 1.54 | 1.54 | 1.54 | 1.54
Number of host CPUs
Number of FMCs
rhost = 600 MB/s
linear_regression
scan
k-means
string_match
linear_regression-XL
scan-XL
k-means-XL
string_match-XL

## Slide 30: Iso-performance curves
When host interface is very fast: host CPUs become more effective, but iSSD is still good!
Chart: 
| 4 | 8 | 12 | 16
linear | 34 | 51.5 | 51.5 | 51.5
string | 27 | 54 | 60 | 60
k-means | 43 | 86.3 | 129 | 172
scan | 6.1 | 6.1 | 6.1 | 6.1
linear-acc | 10.2 | 15.4 | 15.4 | 15.4
string-acc | 19.5 | 39 | 43.5 | 43.5
k-means-acc | 8.8 | 18 | 26.6 | 35.4
scan-acc | 1.54 | 1.54 | 1.54 | 1.54
Number of host CPUs
Number of FMCs
rhost = 600 MB/s
linear_regression
scan
k-means
string_match
linear_regression-XL
scan-XL
k-means-XL
string_match-XL
Chart: 
| 4 | 8 | 12 | 16
 | 34 | 68 | 102 | 136.5
 | 27 | 54 | 80 | 107
 | 43 | 83.3 | 129 | 172
 | 42.7 | 82 | 82 | 82
 | 10.2 | 20.4 | 30.6 | 40.8
 | 19.5 | 39 | 58.5 | 78
 | 8.8 | 18 | 26.6 | 35.4
 | 10.65 | 20.5 | 20.5 | 20.5
Number of host CPUs
rhost = 8 GB/s
linear_regression
scan
k-means
string_match
linear_regression-XL
scan-XL
k-means-XL
string_match-XL
Number of FMCs

## Slide 31: Energy (energy per byte)
iSSD energy benefits are large!
  At least 5× (k-means) and the average is 9+×
Chart: 
| w/o SP | w/ SP | linear
cpu | 8.3267 | 1.6512
sp | 0 | 0.084236
DRAM | 2.1333 | 1.0025
NAND | 0.98125 | 0.98125
Chart: 
| w/o SP | w/ SP | string
cpu | 5.045 | 4.2189
sp | 0 | 0.0080758
DRAM | 2.0362 | 1.3619
NAND | 0.93015 | 0.93015
Chart: 
| w/o SP | w/ SP | kmeans
cpu | 25.2884 | 7.4823
sp | 0 | 0.060206
DRAM | 7.1743 | 1.6277
NAND | 0.92654 | 0.92654
Energy Per Byte (nJ/B)
Chart: 
| host | ISSD w/o SP | ISSD w/ SP | host | ISSD w/o SP | ISSD w/ SP | host | ISSD w/o SP | ISSD w/ SP | host | ISSD w/o SP | ISSD w/ SP | linear_reg. | string_match | k-means | scan | Legend
EPB_host_CPU | 32.8987 | 62.977 | 95.9434 | 3.1941 | 40
EPB_main_mem | 12.4425 | 14.8208 | 13.335 | 11.0662 | 40
EPB_chipset | 20.3394 | 24.2271 | 21.7984 | 18.0896 | 40
EPB_IO | 35.594 | 42.3974 | 38.1471 | 31.6567 | 40
EPB_disk | 2.5448 | 2.7628 | 2.6266 | 2.4186 | 40
EPB_ISSD | 11.4412 | 3.7192 | 8.0113 | 6.5191 | 33.3893 | 10.0968 | 9.9488 | 3.4371
host
CPU
main
memory
I/O
SSD
chipset
NAND
DRAM
Chart: 
| w/o SP | w/ SP | scan
cpu | 1.4285 | 0.77199
sp | 0 | 0.040138
DRAM | 6.9856 | 1.0903
NAND | 0.92654 | 0.92654
host | 0.60812 | 0.60812
processor
I/O
SP

## Slide 32: Summary
Processing large volumes of data is often inefficient on modern systems
iSSD execute limited application functions (or simply new features) to offer high data processing throughput (or other values) at a fraction of energy
iSSD design is different from active disks
  Very high internal bandwidth
  Internal parallelism
  Relative insensitivity to data fragmentation

## Slide 33
* Memory Solutions Lab. (MSL)
Memory Division, Samsung Electronics Co.
Computer Science Department
University of Pittsburgh
Active Disk Meets Flash:
A Case for Intelligent SSDs
Sangyeun Cho*, Chanik Park, Hyunok Oh, Sungchan Kim, Youngmin Yi, Greg Ganger