## Slide 1: A Novel Scalable IPv6 Lookup Scheme Using Compressed Pipelined Tries
Michel Hanna, Sangyeun Cho,
Rami Melhem
Computer Science Department
University of Pittsburgh

## Slide 2: Internet is evolving fast…
Internet bandwidth requirements going up
Bottom line: exchange more packets faster

## Slide 3: IP lookup
Process of determining to which output port an incoming packet must be forwarded in a router
…
input 1
input 2
input N
…
output 1
output 2
output N

## Slide 4: IP lookup
Forwarding Table
Forwarding Decision
Switching Fabric
Prefix | Port #
0* | 0
1* | 1
100* | 0
1000* | 1
100000* | 3
101* | 2
110* | 1
11001* | 0
Process of determining to which output port an incoming packet must be forwarded in a router
On packet arrival, the router uses the incoming packet’s destination address as a key to find the longest matching prefix in the forwarding table

## Slide 5: Our contributions
Observation
  There is a strong spatial locality in the output port address space
  This locality offers a special opportunity to remove the information redundancy in IP forwarding table
Design
  We propose the inter-node compression scheme
Evaluation
  Simulation w/ IPv6 tables and CACTI
  Reduction due to compression ~55%

## Slide 6: Agenda
Current solutions
Our solution: inter-node compressed trie
Quantitative evaluation
Summary

## Slide 7: Current solutions
Algorithm-based
  Uses RAM to store IP lookup data structures (“trie”)
  May require large memory
  Algorithm complexity and memory bandwidth determines throughput
Hardware-based
  Uses TCAM to obtain outcome in a single step
  Parallel search results in high power consumption
  TCAM’s clock frequency typically lower than RAM
  Low bit density and scalability

## Slide 8: Can we do better?
Wish list
  TCAM-like performance
  RAM-like cost, scalability, and power
  Keep up with IPv6 and new ultra high link rates
We take a trie traversal approach w/ pipelined hardware
  Simple time and space bounds
  Uses fast RAM blocks, each being a pipeline stage
However, how do we enumerate leaves and levels? (e.g., IPv6 has 128-bit address)

## Slide 9: Background: binary trie
Trie
  A tree of nodes
  A node is an array of elements
  Each element holds a key or a pointer to another trie node
Binary trie uses a single bit for branching

## Slide 10: Background: binary trie
 | Prefix | Port
a | 000***** | 0
b | 000101** | 1
c | 0001111* | 2
d | 0010**** | 0
e | 00111*** | 2
f | 0110**** | 0
g | 01111*** | 2
h | 1******* | 0
i | 1001**** | 0
j | 11011*** | 2
k | 11011*** | 1
l | 111101** | 1
m | 1111111* | 2
Root
0 | 
1 | h
0 | 
1 | 
0 | a
1 | 
0 | 
1 | b
1 | 
1 | c
1 | 
0 | d
1 | 
1 | 
1 | 
0 | f
1 | 
0 | 
1 | 
1 | j
0 | 
1 | k
1 | 
1 | 
0 | 
1 | l
1 | 
1 | 
0 | 
0 | 
1 | i
1 | 
1 | m
1 | e
1 | g

## Slide 11: Background: multi-bit trie
 | Prefix | Port
a | 000***** | 0
b | 000101** | 1
c | 0001111* | 2
d | 0010**** | 0
e | 00111*** | 2
f | 0110**** | 0
g | 01111*** | 2
h | 1******* | 0
i | 1001**** | 0
j | 11011*** | 2
k | 11011*** | 1
l | 111101** | 1
m | 1111111* | 2
000 | a
001 | -
010 | 
011 | -
100 | h
101 | h
110 | h
111 | h
00 | 
01 | 
10 | -
11 | -
00 | d
01 | d
10 | 
11 | e
00 | 
01 | 
10 | -
11 | j
00 | 
01 | 
10 | -
11 | -
00 | 
01 | 
10 | b
11 | b
00 | 
01 | 
10 | 
11 | c
00 | 
01 | 
10 | l
11 | l
00 | 
01 | 
10 | 
11 | m
00 | 
01 | 
10 | k
11 | k
00 | f
01 | f
10 | 
11 | g
00 | 
01 | 
10 | i
11 | i
Root
Each level covers multiple bits!

## Slide 12: Background: leaf-pushed trie
 | Prefix | Port
a | 000***** | 0
b | 000101** | 1
c | 0001111* | 2
d | 0010**** | 0
e | 00111*** | 2
f | 0110**** | 0
g | 01111*** | 2
h | 1******* | 0
i | 1001**** | 0
j | 11011*** | 2
k | 11011*** | 1
l | 111101** | 1
m | 1111111* | 2
000 | -
001 | -
010 | 
011 | -
100 | -
101 | h
110 | -
111 | -
00 | a
01 | a
10 | -
11 | -
00 | d
01 | d
10 | 
11 | e
00 | h
01 | h
10 | -
11 | j
00 | h
01 | h
10 | -
11 | -
00 | a
01 | a
10 | b
11 | b
00 | a
01 | a
10 | a
11 | c
00 | h
01 | h
10 | l
11 | l
00 | h
01 | h
10 | h
11 | m
00 | h
01 | h
10 | k
11 | k
00 | f
01 | f
10 | 
11 | g
00 | h
01 | h
10 | i
11 | i
Root
Push prefixes downward!

## Slide 13: Background: Lulea trie
Compress a trie by using bitmaps and compressed data vectors
  “Lulea bitmap” [Degermark et al., ’97]
a
a
b
b
1
0
1
0
a
b
bitmap
compressed
data vector
original node
Lulea node

## Slide 14: Agenda
Current solutions
Our solution: inter-node compressed trie
Quantitative evaluation
Summary

## Slide 15: Our solution
Idea: what about using the next hop information (port #) instead of prefixes?
Reality check: # of output ports in an Internet router is limited to few tens
Chart: port number
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | > 7
Equix2 | 67.5583 | 4.1369 | 2.3017 | 9.9222 | 8.9269 | 2.8305 | 0.7776 | 1.0886 | 2.46
Eugene1 | 94.46 | 0.31 | 0.06 | 0.53 | 0.06 | 0.62 | 0.31 | 1.14 | 2.51

## Slide 16: Our “uncompressed trie”
-2 | {a,b,c}
-2 | {d,e}
-1 | {}
-2 | {f,g}
0 | {h,i}
0 | {h}
-2 | {h,j,k}
-2 | {h,l,m}
0 | {a}
0 | {a}
-2 | {a,b}
-2 | {a,c}
0 | {d}
0 | {d}
-1 | {}
2 | {e}
0 | h
0 | h
-2 | {h,k}
2 | j
0 | {h}
0 | {h}
-2 | {h,l}
-2 | {h,m}
0 | {a}
0 | {a}
1 | {b}
1 | {b}
0 | {a}
0 | {a}
0 | {a}
2 | {c}
0 | {h}
0 | {h}
1 | {l}
1 | {l}
0 | {h}
0 | {h}
0 | {h}
2 | {m}
0 | {h}
0 | {h}
1 | {k}
1 | {k}
0 | {f}
0 | {f}
-1 | {}
2 | {g}
Root
Two parts in a node
  Port #
  Prefix list
port #
prefix
list

## Slide 17: Our “uncompressed trie”
-2 | {a,b,c}
-2 | {d,e}
-1 | {}
-2 | {f,g}
0 | {h,i}
0 | {h}
-2 | {h,j,k}
-2 | {h,l,m}
0 | {a}
0 | {a}
-2 | {a,b}
-2 | {a,c}
0 | {d}
0 | {d}
-1 | {}
2 | {e}
0 | h
0 | h
-2 | {h,k}
2 | j
0 | {h}
0 | {h}
-2 | {h,l}
-2 | {h,m}
0 | {a}
0 | {a}
1 | {b}
1 | {b}
0 | {a}
0 | {a}
0 | {a}
2 | {c}
0 | {h}
0 | {h}
1 | {l}
1 | {l}
0 | {h}
0 | {h}
0 | {h}
2 | {m}
0 | {h}
0 | {h}
1 | {k}
1 | {k}
0 | {f}
0 | {f}
-1 | {}
2 | {g}
Root
Two parts in a node
  Port #
  Prefix list
Special port #
  -1 refers to an empty node
  -2 is a pointer to a next-level node

## Slide 18: Inter-node compression
-2 | {a,b,c}
-2 | {d,e}
-1 | {}
-2 | {f,g}
0 | {h,i}
0 | {h}
-2 | {h,j,k}
-2 | {h,l,m}
0 | {a}
0 | {a}
-2 | {a,b}
-2 | {a,c}
0 | {d}
0 | {d}
-1 | {}
2 | {e}
0 | h
0 | h
-2 | {h,k}
2 | j
0 | {h}
0 | {h}
-2 | {h,l}
-2 | {h,m}
0 | {a}
0 | {a}
1 | {b}
1 | {b}
0 | {a}
0 | {a}
0 | {a}
2 | {c}
0 | {h}
0 | {h}
1 | {l}
1 | {l}
0 | {h}
0 | {h}
0 | {h}
2 | {m}
0 | {h}
0 | {h}
1 | {k}
1 | {k}
0 | {f}
0 | {f}
-1 | {}
2 | {g}
Root
Step 1
  Replace prefixes with their port numbers

## Slide 19: Inter-node compression
Step 1
  Replace prefixes with their port numbers
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -2
 | 2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | -1
 | 2
CRoot

## Slide 20: Inter-node compression
Step 1
  Replace prefixes with their port numbers
Note that many nodes have the same contents
Next step
  Starting from leaves to root, remove redundant nodes
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -2
 | 2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | -1
 | 2
CRoot

## Slide 21: Inter-node compression
We are done with the leaf level!
Let’s move onto the next level
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -2
 | 2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | -1
 | 2
CRoot

## Slide 22: Inter-node compression
The entire trie is now compressed…
  We call this “inter-node compressed trie” (INCT)
  Move to forwarding plane
In this example we save 50% of the nodes, not counting the root
Also in the paper
  Detailed algorithm
  Sketch of incremental update
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | -1
 | 2
CRoot
Notes: In this example, we were able to save 50% of the nodes (not counting the root).
for the root we may use the Lulea compression.

## Slide 23: Agenda
Current solutions
Our solution: inter-node compressed trie
Quantitative evaluation
Summary

## Slide 24: IPv6 tables
We use simulation to validate our scheme on 10 real-life IPv6 tables
Name | Size | H* | Name | Size | H*
Equix 1 | 3,189 | 9 | Linx 2 | 37,282 | 13
Equix 2 | 3,215 | 9 | Quagga 1 | 3,464 | 7
Eugene 1 | 3,211 | 16 | Quagga 2 | 3,299 | 4
Eugene 2 | 3,233 | 15 | Wide 1 | 5,412 | 2
Linx 1 | 36,366 | 13 | Wide 2 | 5,470 | 2
H*: # of unique ports

## Slide 25: # INCT levels vs. total memory
Chart: # INCT trie levels
| 5 | 6 | 7 | 8 | 9
Linx2 | 8988 | 2044.5 | 804 | 389 | 295
Eugene1 | 4986 | 1077 | 427 | 179 | 140
Use 7 levels (total memory vs. delay)

## Slide 26: Impact of compression
Chart: total memory (KB)
| AVE. | Equix1 | Equix2 | Eugene1 | Eugene2 | Linx1 | Linx2 | Qugga1 | Qugga2 | Wide1 | Wide2
Uncompressed(7) | 1041.9 | 540 | 514 | 627 | 300 | 2127 | 1945 | 892 | 320 | 1576 | 1578
INCT(7) | 465.6 | 350 | 375 | 427 | 185 | 857 | 804 | 480 | 206 | 456 | 516
A compression ratio of 44.7% on average

## Slide 27: INCT vs. other compression schemes
Chart: total memory (MB)
| AVE. | Equix1 | Equix2 | Eugene1 | Eugene2 | Linx1 | Linx2 | Qugga1 | Qugga2 | Wide1 | Wide2
Lulea/Tree Bitmap(6) | 5.2763 | 2.9346 | 3.2432 | 3.5234 | 1.6348 | 8.4443 | 8.1553 | 5.1465 | 2.0967 | 7.7148 | 7.5273
INCT(6) | 1.7454 | 1.6865 | 1.7266 | 1.8535 | 1.2656 | 2.1221 | 2.0791 | 1.8145 | 1.373 | 1.7793 | 1.6953
MIPS(57) | 0.33115 | 0.16211 | 0.18164 | 0.18359 | 0.099609 | 0.63672 | 0.63477 | 0.20117 | 0.10645 | 0.5498 | 0.55566
Binary INCT(57) | 0.038184 | 0.023438 | 0.027344 | 0.027344 | 0.014648 | 0.066406 | 0.069336 | 0.02832 | 0.015625 | 0.051758 | 0.057617
INCT(6) smaller than Lulea(6) by 67%
Binary INCT(57) smaller than MIPS(57) by 88%
With 6 strides: {16,16,8,8,8,8}
MIPS also exploits limited # of ports; uses “independent” prefixes to store in arbitrary order in TCAM; w/ strides of {8,1,1,1,…,1}

## Slide 28: Performance and cost
 | Uncompressed(7) | INCT(7) | Savings or Loss
Total RAM size (MB) | 2.11 | 0.85 | 59.7%
Total access time (ns) | 3.74 | 2.85 | 23.8%
Pipeline frequency (GHz) | 5.29 | 4.90 | -7.4%
Total read dynamic energy (nJ) | 0.09 | 0.05 | 44.4%
Total read dynamic power at max frequency (W) | 0.54 | 0.29 | 46.3%
Total area (mm2) | 5.42 | 2.14 | 60.5%

## Slide 29: Agenda
Current Solutions & Our Approach
What is a “Trie”
Our Matchless Trie Scheme
Simulation Results
Summary

## Slide 30: Summary
We proposed a novel trie data compression method (INCT) to enable efficient pipelined hardware implementation
Our “matchless” approach using INCT has the potential of achieving 3.1 Tbps throughput
We find that our scheme compares favorably with other compression methods
  Our scheme is also much more power efficient and scalable than TCAM

## Slide 31: A Novel Scalable IPv6 Lookup Scheme Using Compressed Pipelined Tries
Michel Hanna, Sangyeun Cho,
Rami Melhem
Computer Science Department
University of Pittsburgh

## Slide 32: Incremental update
INCT uses a fixed stride trie  use write bubble
  Upon receiving an update request, the router’s control plane calculates how many nodes will be affected
  It sends special messages (write bubbles) to each affected node in the forwarding plane
After some time, we have to re-make the entire trie
  This depends on how big the trie becomes

## Slide 33: Incremental Updates: 2
1
2
2
3
2
Root
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | -2
 | 2
trimmed trie
CRoot
 | -2
 | -2
 | -1
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | -2
 | -2
 | 0
 | 0
 | 0
 | 2
 | 0
 | 0
 | 1
 | 1
 | 0
 | 0
 | -1
 | 2
 | 0
 | 0
 | -2
 | 2
control plane
INCT trie
forwarding plane
back & forward pointers
cross pointer
1