## Slide 1: Memorage: Emerging Persistent RAM based Malleable Main Memory and Storage Architecture
Juyoung Jung and Sangyeun Cho
Computer Science Department
University of Pittsburgh

## Slide 2: Introduction
Conventional memory hierarchy
Secondary Storage
Main Memory
DRAM
HDD

## Slide 3: Introduction
Conventional memory hierarchy
DRAM
HDD
High performance
Low cost per bit
Scaling
Power consumption
Slow performance improvement

## Slide 4: Emerging Persistent RAMs (PRAM)
 | Properties | Design Implications
 | Scalable | Higher density
 | Energy efficient | Energy saving
 | Byte-addressable | Main memory
 | Persistent | Secondary storage
 | Slower | Architectural support needed !
 | Imbalanced Read/Write | 
 | Limited cell endurance | 
1
2
(PRAM Storage Device)

## Slide 5: Outline
Introduction
PRAM-based System Model
Memorage Architecture
Experimental Results
Conclusion

## Slide 6: Future PRAM-based System Model
Memory Bus
PSD
CPU
PRAM
Main
Memory
Secondary
Storage
Legacy I/O interface via
Platform Controller Hub
(SLC)
(MLC)
Easy adoption without big change
Familiar dichotomized memory hierarchy concept

## Slide 7: Problem of Memory Pressure
Memory Bus
PSD
CPU
PRAM
Main
Memory
Secondary
Storage
Legacy I/O interface via
Platform Controller Hub
Ever-growing memory demands
Memory Pressure
Severe performance degradation during page swapping operation

## Slide 8: Outline
Introduction
PRAM-based System Model
Memorage Architecture
  Objective and observations
  Memorage approaches
  Design and implementation
Experimental Results
Conclusion

## Slide 9: Memorage Architecture
Objectives
  Effective handling of memory pressure
  Extending system lifetime
System-level observations
  Little characteristic distinctions between main memory and storage resources (both are PRAMs)
  Reducing I/O software overhead becomes more important than in the past
  Storage density grows exponentially but the available storage capacity underutilized

## Slide 10: Outline
Introduction
PRAM-based System Model
Memorage Architecture
  Objective and observations
  Memorage approaches
  Design and implementation
Experimental Results
Conclusion

## Slide 11: Memorage Architecture
Flexible resource sharing
  Cross the traditional memory hierarchy boundary
Memorage approaches
  Don’t swap, give more memory
    Under high memory pressure, borrow PRAM resources from PSD to cope with the memory deficit
  Don’t pay for physical over-provisioning
    Excess PSD resources provide a system with “virtual” over-provisioning

## Slide 12
OS VM manger
Memorage Resource Controller
PSD
device driver
File system
Memory subsystem
Storage subsystem
Memorage system
Step1-1
Step1-2
Step2
case(a)
Step2
case(a)
Memory Pressure
Okay! I have some to lend

## Slide 13
OS VM manger
Memorage Resource Controller
PSD
device driver
File system
Memory subsystem
Storage subsystem
Memorage system
Step1-1
Step1-2
Step2
case(b)
Do swap and
Page reclamation
Memory Pressure
Sorry! I have a tight budget

## Slide 14: Outline
Introduction
PRAM-based System Model
Memorage Architecture
  Objective and observations
  Memorage approaches
  Design and implementation
Experimental Results
Conclusion

## Slide 15: Key Design Goals
Transparency to existing applications
  Avoid re-compiling applications
Manageable required system changes
  Fast adoption of Memorage architecture
  Extensive reuse of existing VMM infrastructures
Low system overhead
  Keep users oblivious to Memorage support

## Slide 16: Managing Resource Information
1. PSD resource detection
Physical PSD PRAM
chunk0
chunkN
chunk1
2. Building PSD resource data structures
node
DMA
DMA32
NORMAL
MEMORAGE
zone
from main memory
detected during boot process
from PSD
Reuse memory hot-plug feature !!

## Slide 17: Managing Resource Information
3. PSD resource transfer
Physical PSD PRAM pages
chunk0
chunkN
chunk1
MEMORAGE
zone
Filesystem
manipulation

## Slide 18: File system Metadata Exposure
Boot block
Block group 0
Block group 1
Block group n
···
Super block
Group descriptors
Data
bitmap
Inode
bitmap
Inode
table
Data
blocks
Zone
Memorage
···
···
Buddy allocator including new zone Memorage
Exposed to Memorage manager
1111111 0000000000 00110
···
1111111 1111111111 00110
···
···
···
Example of data bitmap change on storage capacity donation
(4MB donation assuming 4KB data block size)
On-disk layout of ext3 file system

## Slide 19: Memory Expansion and Shrinkage
2
1
pages_high
pages_low
pages_min
new pages_high
new pages_low
new pages_min
kswapd woken up
zone balanced
kswapd sleep
time
Total size
Available MM pages
Additional
Memorage pages
With Memorage, never reach to watermark to invoke kswapd in this case
expanded margin

## Slide 20: Outline
Introduction
PRAM-based System Model
Memorage Architecture
Experimental Results
Conclusion

## Slide 21: Evaluation Methodology
Performance evaluation
  Measure the performance improvement with a prototype system implemented in Linux
  Emulate future platform with NUMA system

## Slide 22: Emulation Methodology
CPU #0
(4 cores)
CPU #1
(4 cores)
4GB
Socket 0 memory
96GB
Socket 1 memory
Main memory
Emulated PSD
Offloading PSD resources
Memorage performs hot-plug PSD resources
Memory pressure

## Slide 23: OS Latency for Page Fault Handling
58.6 us
21.6 us

## Slide 24: Evaluated Memory Configuration
Workload
  8 memory-intensive benchmarks from SPEC CPU2006
  Aggregate memory footprint is 5.6GB
(bwaves, mcf, milc, zeusmp, cactusADM, leslie3d, lbm, GemsFDTD)
Memory configurations
  Baseline: 4.4GB effective memory capacity available
  Memorage: with additional 2GB capacity from PSD, total 6.4GB effective memory capacity available

## Slide 25: Exec. Time Breakdown (Baseline)
Chart: Execution Time Breakdown for User vs. Kernel in %
| bwaves | cactusADM | GemsFDTD | lbm | leslie3d | mcf | milc | zeusmp
Kernel Time | 487.4867 | 487.6133 | 285.47 | 21.0667 | 78.6933 | 729.4667 | 407.8133 | 470.82
User Time | 1337.977 | 1862.953 | 1238.573 | 964.51 | 1235.723 | 907.34 | 1059.88 | 1217.347

## Slide 26: Exec. Time Breakdown (Memorage)
Chart: Execution Time Breakdown for User vs. Kernel in %
| bwaves | cactusADM | GemsFDTD | lbm | leslie3d | mcf | milc | zeusmp
Kernel Time | 7.87 | 7.6767 | 4.67 | 4.03 | 4.4833 | 5.0133 | 21.67 | 4.7333
User Time | 1541.083 | 1836.167 | 1336.973 | 1099.433 | 1306.84 | 1160.02 | 1244.513 | 1301.447

## Slide 27: Relative Performance of Benchmark
dynmic

## Slide 28: Lifetime Evaluation
  Analytical model for lifetime analysis
Variable | Description
Lm , Ls | lifetime of main memory(MM) and PSD
Cm , Cs | capacity of MM and PSD
Em , Es | write endurance of MM and PSD
Dm , Ds | total data volume of MM and PSD before the first failure Dm = Em ∙ Cm , Ds = Es ∙ Cs
Bm , Bs | average data update rate or write data band width
α , β, ϒ | Cm = α ∙ Cs , Bs = β∙ Bm , Em = ϒ ∙ Es
h | η / Cm , where η is the transfer size

## Slide 29: Main Memory Lifetime Improvement
variables
endurance ratio fixed
rapidly reaches a maximum lifetime even with small bandwidth ratio
Since realistic write bandwidth of main memory is much larger than PSD, achieve large main memory lifetime improvement !!
8GB MM + 240GB PSD
8GB MM + 480GB PSD

## Slide 30: System Lifetime
2x memory lifetime improvement
1000x PSD lifetime degradation
Es = 105, Em = 106, Bm = 100MB/s
PSD lifetime from 10,000 years to 10 years
Main memory lifetime from 2.5 year to 5 years
ratio of the donated PSD capacity to memory capacity

## Slide 31: Outline
Introduction
PRAM-based System Model
Memorage Architecture
Experimental Results
Conclusion

## Slide 32: Conclusion
Memorage architecture
  Capacity sharing across the conventional memory and storage boundary
  Better handle memory pressure by exploiting excess PRAM resources from PSD
    System performance improvement up to 40.5%
  Better utilize available system PRAM resources to improve main memory lifetime
    System lifetime enhancement up to 6.9 times

## Slide 33: Thank you for listening!