## Slide 1: Accurately Approximating Superscalar Processor Performance from Traces
Kiyeon Lee, Shayne Evans, and Sangyeun Cho
Dept. of Computer Science
University of Pittsburgh

## Slide 2: Motivation
How to simulate the dynamic behavior of superscalar processor?
  Execution-driven simulation
  Trace-driven simulation with full trace
  Trace-driven simulation with filtered trace?
  Use timing-aware L1 filtered traces to predict a core’s dynamic behavior
Goal:
  Accurate trace-driven simulation using storage efficient filtered traces
    Perfect branch prediction and instruction cache is used
  Form a baseline study of multicore simulation at an early design stage using traces

## Slide 3: Our contributions
Three trace-driven simulation models with L1 filtered traces
  L1 filtered traces are generated with perfect L2 cache
Model 1: Isolated Cache Miss Model (IsoCMM)
  No MLP (Memory Level Parallelism)
  Assume every L1 dcache miss is isolated
  Pessimistic when scheduling trace items
Model 2: Independent Cache Miss Model (IndepCMM)
  MLP
  Assume every L1 dcache miss is independent
  Optimistic when scheduling trace items
Model 3: Pairwise Dependent Cache Miss Model (PDepCMM)
  MLP
  Built on top of independent cache miss model
  Honors dependency between trace items

## Slide 4: Isolated cache miss model
Sequentially process each trace item
  Update statistics and access L2 cache
If L2 cache miss occurs, return the estimated impact of L2 cache miss to the program execution time
Real impact of L2 cache miss on address A to the program execution time
  Trun 2 – Trun 1
  smaller than memory access latency
run 1
run 2
A
L1 miss, L2 hit
L1 miss, L2 miss

## Slide 5: Instruction permeability analysis
Assume all L1 dcache misses are isolated
run 1
(perfect L2)
run 2
run3
…
…
…
a1 cycles
trace item
(n)
trace item
(n+1)
…
…
…
b1 cycles
A
L1 miss, L2 hit
L1 miss, L2 miss
B
A
B
B
A
trace simulation
Hit on addr. A a1 cyclesMiss on addr. A b1 cycles
C
C
C
a2 cycles
c2 cycles
a3 cycles
b3 cycles
D
D
D
trace item
(n+2)
trace item
(n+3)
trace simulation
Hit on addr. B a2 cyclesMiss on addr. B c2 cycles
trace simulation
Hit on addr. C a3 cyclesMiss on addr. C b3 cycles

## Slide 6: Accuracy of isolated cache miss model
high L1 dcache miss rate + clustered L1 dcache misses
Chart: CPI error
| mcf | art | gcc | ammp | perl | facerec
naïve | 1 | 1 | 0.72 | 0.47 | 0.11 | 0.03
IsoCMM | 0.76 | 1 | -0.01 | -0.06 | 0.00014458 | 0
low L1 dcache miss rate + sparse L1 dcache misses

## Slide 7: Weakness of isolated cache miss model
Memory accesses are processed sequentially (no possible MLP)
  Impact of L2 cache misses are accumulated
  Superscalar processor can overlap multiple independent memory accesses
Our approach:
Consider MLP
Use a model that can overlap memory accesses
  Model 2: Independent cache miss model

## Slide 8: How to process trace items in parallel?
Instructions can be issued after being placed in reorder buffer (ROB)
Assign a unique ROB sequence ID for every instruction
Estimate which trace items can be processed in parallel by comparing the ROB sequence ID in the trace items
inst
#1
64-entry Reorder Buffer
…
inst
#35
inst
#64
…
inst
#80
…
…
…
inst
#1
inst
#35
inst
#64
inst
#80
…
Trace file

## Slide 9: Independent cache miss model
L1 misses are assumed to be independent
run 1
…
5 cycles
15 cycles
20 cycles
8 cycles
A (2)
B (10)
C (40)
D (85)
E (90)
L1 miss, L2 miss
64-entry Reorder Buffer
…
C
#40
…
A
#2
B
#10
…
trace item B and C can be processed according to the # cycles recorded in its trace item
B
#10
…
C
#40
…
trace item D can be processed after trace item B commits
C
#40
…
D
#85
blocked!
still blocked
trace item E can be processed according to the # cycles recorded in the trace item
E
#90
64-entry Reorder Buffer
…
…

## Slide 10: Accuracy of Independent cache miss model
80% of trace items have dependencies
Chart: CPI error
| mcf | art | gcc | ammp | perl | facerec
naïve | 1 | 1 | 0.72 | 0.47 | 0.11 | 0.03
IndepCMM | -0.2 | -0.058328 | -0.19105 | -0.0010048 | -0.0017502 | -0.00073269

## Slide 11: Weakness of independent cache miss model
Can be too optimistic!
Dependencies between trace items have to be considered
Our approach:
A model that honors the dependency between trace items
  Model 3: Pairwise dependent cache miss model
inst
#1
…
Inst
#35
…
Inst
#64
dependent

## Slide 12: Pairwise dependent cache miss model
Based on the independent cache miss model
Honor the dependency between trace items
run 1
…
5 cycles
15 cycles
20 cycles
8 cycles
A (2)
B (10)
C (40)
D (85)
E (90)
L1 miss, L2 miss
64-entry Reorder Buffer
trace item E has to wait until trace item D gets resolved
C
#40
…
D
#85
E
#90
…
…
dependency

## Slide 13: Accuracy of Pairwise dependent cache miss model
Chart: CPI error
| mcf | art | gcc | ammp | perl | facerec
IndepCMM | -0.2 | -0.058328 | -0.19105 | -0.0010048 | -0.0017502 | -0.00073269
PDepCMM | 0.0025187 | 0.0021925 | -0.021094 | 0.02518 | -0.0017479 | -0.00071387

## Slide 14: Accuracy of Pairwise dependent cache miss model
simulation speedup of 30.7x on average
Chart: CPI error
| mcf | gzip | vpr | twolf | gcc | crafty | parser | bzip2 | perl | vortex | gap | eon | art | galgel | equake | swim | ammp | applu | lucas | mgrid | apsi | fma3d | facerec | wupwise | mesa | sixtrack | RMS error
PDepCMM | 0.0025187 | 0.0063299 | 0.010459 | -0.016754 | -0.021094 | 0.0015922 | -0.1 | -0.019168 | -0.0017479 | -0.0027231 | -0.1 | 0.0010837 | 0.0021925 | 0.01424 | -0.061872 | 0.013428 | 0.02518 | 0.014275 | 0.027771 | 0.013038 | -0.016776 | 0.0065878 | -0.00071387 | 0.0062104 | -0.0070881 | 0.0056566 | 0.047976
why?

## Slide 15: Dependency issues
L1 dcache delayed hits are included in the trace file in addition to the L1 dcache misses.
delayed hits
delayed hits
with long
memory access latencies
with
perfect L2 cache
cache hits
Subsequent accesses to the same cache block B
A L1 dcache miss
on cache block B
Large CPI errors due to dependencies can be reduced by considering all potential dependencies between trace items

## Slide 16: Accuracy of Pairwise dependent cache miss model
simulation speedup of 30.7x on average
Chart: CPI error
| mcf | gzip | vpr | twolf | gcc | crafty | parser | bzip2 | perl | vortex | gap | eon | art | galgel | equake | swim | ammp | applu | lucas | mgrid | apsi | fma3d | facerec | wupwise | mesa | sixtrack | RMS error
PDepCMM | 0.0025187 | 0.0063299 | 0.010459 | -0.016754 | -0.021094 | 0.0015922 | -0.1 | -0.019168 | -0.0017479 | -0.0027231 | -0.1 | 0.0010837 | 0.0021925 | 0.01424 | -0.061872 | 0.013428 | 0.02518 | 0.014275 | 0.027771 | 0.013038 | -0.016776 | 0.0065878 | -0.00071387 | 0.0062104 | -0.0070881 | 0.0056566 | 0.047976
Can we apply pairwise dependent cache miss model to a multicore system simulation?
Two important questions need to be answered

## Slide 17: Does our model preserve a processor’s dynamic behavior?
Can the model predict how shared resources (e.g., L2 cahce) are temporally used by multiple superscalar cores?
All six benchmarks showed at least 93.5% similarity
Chart: gcc
| 0 - 15 | 16 - 31 | 32 - 47 | 48 - 63 | 64 - 79 | 80 - 95 | 96 - 111 | 112 - 127 | 128 - 143 | 144 - 159 | 160 - 175 | 176 - 191 | 192 - 207 | 208 +
execution-driven | 36.7 | 2.7 | 1.1 | 0.65 | 0.59 | 0.58 | 0.44 | 0.16 | 0.15 | 0.42 | 0.45 | 0.36 | 0.15 | 52.88
trace-driven | 39.74 | 4.42 | 1.76 | 0.86 | 0.88 | 0.56 | 0.49 | 0.26 | 0.19 | 0.51 | 0.57 | 0.44 | 0.16 | 46.57
93.5% similarity

## Slide 18: Can the model accurately project the relative performance?
Given the baseline configuration, can the pairwise dependent cache miss model accurately project the performance of different configurations compared to the baseline configuration?
Conf. 1: Larger L2 cache
Conf. 2: Smaller L2 cache
Conf. 3: Faster memory
Conf. 4: Slower memory
Conf. 5: Slower L2 cache
 | Conf. 1 | Conf. 2 | Conf. 3 | Conf. 4 | Conf. 5
Avg. error | 1.2% | 2.0% | 2.0% | 2.0% | 1.7%

## Slide 19: Conclusions
Introduced three strategies using filtered traces to predict superscalar processor performance from traces
Pairwise dependent cache miss model is the best among the three
  Can accurately predict superscalar processor performance (4.8% RMS error)
  Simulation speedup of 30.7x on average when running spec2k benchmark suite in our current implementation
Our model is amenable for use in multicore simulations targeting multiprogrammed workloads.
  Preserves processor cores' dynamic resource usage behaviors
  Predicts relative performance with precision

## Slide 20: Accurately Approximating Superscalar Processor Performance from Traces
Questions ?