## Slide 1: In-N-Out: Reproducing Out-of-Order Superscalar Processor Behavior from Reduced In-Order Traces
Kiyeon Lee and Sangyeun Cho

## Slide 2: Performance modeling in the early design stages
What we want:
  Fast speed/proof-of-concept
  Study the early design tradeoffs
Processor core configuration?
L2 cache design?
Memory controller?
Computer architect
In-N-Out

## Slide 3: Processor simulation can be slow
gcc (in spec2k) with a small input
  Measured on a 3.8GHz Xeon based Linux box w/ 8GB memory
Case
Time (second)
Ratio to
“native”
Ratio to
“functional”
Native
1.054
1
sim-fast
167
158
1
sim-outorder
4,247
4,029
25
simics (bare)
461
437
1
simics w/ ruby
41,245
39,131
89
simics w/ ruby + opal
155,621
(≈ 43 hours)
147,648
338
We need a faster and yet accurate simulation method

## Slide 4: Contributions
We propose a practical simulation method for modeling superscalar processors
  It’s fast! (in the range of MIPS)
  Identifies optimal design points
Processor abstraction with reduced in-order trace

## Slide 5: Abstraction model
Abstract processor core
L2 cache
Main memory
Superscalar processor
core
trace
trace
Filtered
traces
out-of-order
issue
instruction
fetch & decode
update & commit instruction
limited
hardware sizes

## Slide 6: Talk roadmap
Motivation/contributions
In-N-Out
Evaluation results
Conclusion

## Slide 7
Overall structure and key ideas
IN – N – OUT
1
2
3
2
3
1

## Slide 8: In-N-Out: overall structure
Trace generator: a functional cache simulator
  In-order trace generation
Trace simulator:
  Out-of-order trace simulation
trace
trace
L1 filtered
traces
Functional
cache simulator
trace simulator
target machine
definition
simulation
result
program
program
input
ROB occupancy
analysis

## Slide 9: Challenge 1: reproducing memory-level parallelism
non-mem instr
L1 miss, L2 miss
A
B
C
D
E
A
B
C
D
E
independent
dependency

## Slide 10: Challenge 1: reproducing memory-level parallelism
Exploit the limited reorder buffer (ROB) size
trace file
64-entry ROB
inst
#1
inst
#30
inst
#64
inst
#1
inst
#30
inst
#64
inst
#70
inst
#80
inst
#90
inst
#100
inst
#100
inst
#70
inst
#80
inst
#90
inst
#64
inst
#70
inst
#80
inst
#30
inst
#90
inst
#100
head
tail

## Slide 11: Challenge 1: reproducing memory-level parallelism
Exploit the inherent data dependency between instructions
64-entry ROB
inst
#1
inst
#30
inst
#64
inst
#100
inst
#70
inst
#80
inst
#90
dependent
Our solution: ROB occupancy analysis
- Reconstruct ROB during trace simulation
- Honor the dependency between trace items

## Slide 12: Challenge 2: estimating instruction execution time
  Trace generator is a functional cache simulator
  How do we estimate the instruction execution time?

## Slide 13: Challenge 2: our solution
Instruction data dependency gives a lower-bound
Instruction execution time ≥ 8 cycles
Our solution: Exploit instruction data dependency
- Use a fixed size dependency monitoring window

## Slide 14
Filtered trace simulation
IN – N – OUT
1
2
3
2
3
1

## Slide 15: Preparing L1 filtered traces
ISN = I
n_cycles
type
addr
parent
item #N
ISN = I + 8
n_cycles = 3
type = ld
addr=0x0220
parent = I
item #(N+1)
Ncycles = 3
non-trace item instr
L1 miss (trace item)
Dependency

## Slide 16: Filtered trace simulation
A, B, and D are independent trace items
C depends on B
ROB size: 64 entries
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…

## Slide 17: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
A
(2)
L2 cache
ROB
@ cycle Tdispatch - A

## Slide 18: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
A
(2)
B
(52)
B dispatch time =Tdispatch-A +
L2 cache

## Slide 19: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
A
(2)
65
B
(52)
…
L2 cache
@ cycle Tcommit-A

## Slide 20: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
B
(52)
C
(74)
65
D
(94)
L2 cache
C dispatch time = Tcommit-A +
D dispatch time = Tcommit-A +

## Slide 21: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
65
B
(52)
C
(74)
D
(94)
L2 cache
B commit time = MAX(T1, T2)
T1 = Tcommit-A + MAX( , 18)
T2 = Treturn-B + 1

## Slide 22: Filtered trace simulation
…
A (2)
non-trace item instr
L1 miss (trace item) & L2 miss
B (52)
…
C (74)
…
D (94)
Ncycles = 18
Ncycles = 8
Ncycles = 4
…
65
B
(52)
C
(74)
D
(94)
L2 cache

## Slide 23
Preliminary evaluation results
IN – N – OUT
1
2
3
2
3
1

## Slide 24: Setup
Used spec2k benchmarks
Trace generation
  dependency monitoring window size: 8 instructions
Simplified processor configuration
  Perfect i-cache and branch prediction
In-N-Out (tsim) compared with sim-outorder (esim)

## Slide 25: Evaluation 1: CPI error
CPI error = (CPItsim – CPIesim)/CPIesim
Average (mean of the absolute CPI errors): 7%
  Memory intensive benchmarks show low CPI errors
    mcf (0%), art (4%), and swim (0%)
  Range: -19% ~ 23%

## Slide 26: Evaluation 2: relative CPI change
Relative CPI change = (CPIconf2 – CPIconf1)/CPIconf1
Used to study the design tradeoffs
CPI change after adding artifacts:
  L2 MSHR (Miss status holding register)
    Limits the number of outstanding memory accesses
  L2 data prefetching

## Slide 27: Effect of L2 MSHRs
Compared with unlimited L2 MSHRs
Chart: fma3d
| 4 MSHRs | 8 MSHRs | 16 MSHRs
esim | 1.6 | 1.5084 | 0.18014
tsim | 1.6 | 1.3631 | 0.17577

## Slide 28: Effect of L2 data prefetching
Compared with no L2 data prefetching
Chart: Relative CPI change
| prefetch-on-miss | tagged prefetch | stream prefetch
esim | -0.28834 | -0.39874 | -0.17233
tsim | -0.21522 | -0.312 | -0.17615
equake

## Slide 29: Evaluation 3: relative CPI difference
Relative CPI difference =
|relative CPI change (esim) – relative CPI change (tsim)|
Compares the relative CPI change amount between simulators
  The direction was always identical!

## Slide 30: Effect of uncore parameters
Relative CPI difference (on average) < 3%
Chart: Relative CPI difference
| smaller L2 | larger L2 | faster mem. | slower mem. | slower L2 | different L2 prefetcher
average | 0.028 | 0.006 | 0.012 | 0.008 | 0.021 | 0.029

## Slide 31: Evaluation 4: preserving superscalar processor behavior
Chart: gcc
| 0-12 | 13-24 | 25-36 | 37-48 | 49-60 | 61-72 | 73-84 | 85-96 | 97-108 | 109 + | 0 - 100M
esim | 55.11 | 5.84 | 1.05 | 0.52 | 0.66 | 0.59 | 0.47 | 0.5 | 0.44 | 34.82
tsim | 56.16 | 5.48 | 0.8 | 0.67 | 0.58 | 0.79 | 0.6 | 0.36 | 0.19 | 34.37
25 out of 26 benchmarks showed over 90% similarity

## Slide 32: Simulation speed
156MIPS (Million instructions per second) on average (geometric mean)
  Measured on a 2.26GHz Xeon-based Linux box w/ 8GB memory
  Range: 10MIPS (mcf) to 949MIPS (sixtrack)
Speedup over an execution-driven simulator
  115x faster than sim-outorder

## Slide 33: Case study: Change prefetcher config.
esim tsim
Stream prefetcher configuration
Chart: 
| (64, 4) | (32, 4) | (16, 2) | (8, 1) | (4, 1)
esim | 0.65168 | 0.67769 | 0.65864 | 0.84643 | 0.83633
tsim | 0.67573 | 0.73359 | 0.72435 | 0.8929 | 0.8919
Average CPI

## Slide 34: Case study: Change L2 cache assoc.
esim tsim
L2 cache associativity
Average CPI
Chart: 
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0
esim | 0.75351 | 0.6476 | 0.63313 | 0.62168 | 0.62081
tsim | 0.73291 | 0.63273 | 0.61989 | 0.6083 | 0.60784

## Slide 35: Summary
In-N-Out: a simulation method
  Quickly and accurately models an out-of-order superscalar processor performance with reduced in-order trace
  Identifies optimal design points
  Preserves the dynamic uncore access behavior of a superscalar processor
Simulation speed: 156MIPS (on average)

## Slide 36: Thank you !