## Slide 1: RDIS: A Recursively Defined Invertible Set Scheme to Tolerate Multiple Stuck-At Faults in Resistive Memory
Rami Melhem, Rakan Maddah and Sangyeun cho
Computer Science Department
University of Pittsburgh

## Slide 2: Introduction
DRAM is facing physical limitations that is expected to hinder its scalability
Resistive memories e.g. Phase Change Memory(PCM) are regarded as a promising replacement for DRAM
PCM is characterized by its scalability and density
Initial measurements indicate that PCM is competitive to DRAM in terms of read/write latency and power efficiency.

## Slide 3: Challenges
Write endurance is one of the main causes precluding the adoption of PCM
PCM Cells endure 106 to 108 write operations on average
Repeated writes cause the cells to fail and get stuck permanently at either 0 or 1
  A faulty cell can still be read but not reprogrammed
Variable lifetime of cells due to process variation

## Slide 4: Remedies
Spreading the write evenly across the entire physical space i.e. wear leveling
Suppressing unnecessary writes e.g. silent writes
Multi-bit error correction schemes

## Slide 5: Contribution
RDIS: an error correction scheme for stuck-at faults prominent in resistive memories like PCM
RDIS exploits the stuck-at fault model exhibited by hard-faults in SLC PCM:
  A worn-out cell can be classified as either stuck-at-right(SA-R) or stuck-at-wrong(SA-W) depending on the data pattern
SA-1 | SA-0
0 | 0
Write
SA-W | SA-R

## Slide 6: Goal
Identify a set containing all the SA-W cells
A simple way to build the set is to keep a list of pointers to the SA-W cells
RDIS introduces a systematic method for building the set allowing it to include NF cells
Pointer 1
Pointer 2
How?
Pointer 1
Pointer 2

## Slide 7: RDIS Encoding Process
16 cells
 | 1 |  | 0
 |  |  | 1
2-D Mapping
4 X 4
1
0
1
Stuck-at Cells

## Slide 8: RDIS Encoding Process
Introduce an auxiliary flag for each row and column
  Set the flags for each row and column containing a Stuck-at-wrong cell
  Form a mesh of cells where each cell have its corresponding column and row flags both set
0
1
1
0
1
1
0
0
VX
VY
Mesh
1
1
VX
1
1
VY
SA-W
SA-R
NF
Mesh

## Slide 9: RDIS Fault Masking
Write data inverted within the initial mesh
  Stuck-at cells switch roles: SA-W  SA-R and SA-R  SA-W
  Set auxiliary flags accordingly and form a new mesh
  Recursively apply the same process until mesh size becomes zero i.e. no SA-W cells
1
1
VX
1
1
VY
invert
1
0
VX
1
0
VY
0
VX
0
VY
invert
New mesh
Done!
SA-W
SA-R
NF

## Slide 10: RDIS Fault Masking
After reducing the mesh size to zero, this is how the original 2D data block will look like:
 | 1 |  | 0
 |  |  | 1
0
2
1
0
VX
2
1
0
0
VY
Data Retrieval?

## Slide 11: Data Retrieval/Decoding
To retrieve data, read the value of a cell inverted if the minimum of its corresponding row and column counters is odd
0
2
1
0
VX
2
1
0
0
VY
Min is odd, read inverted!
Min is even, read un-inverted!
Invertible Set!

## Slide 12: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 13: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 14: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 2
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 2
0 | 1 | 0 | 2 | 2 | 0 | 2 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 15: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 2
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 3
0 | 1 | 0 | 2 | 3 | 0 | 3 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 16: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 2
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 3
0 | 1 | 0 | 2 | 3 | 0 | 3 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 17: Another Example
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 2
 |  |  |  |  |  |  |  | 1
 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | 3
0 | 1 | 0 | 2 | 3 | 0 | 3 | 0 | 
VX
VY
SA-W
SA-R
NF
Mesh
Invertible Set

## Slide 18: RDIS Coverage
RDIS guarantees the recovery from three stuck-at faults
However, RDIS can effectively recovery from much more faults beyond what it guarantees with a high probability
2 sources for halting:
  The stuck-at faults form a cycle
  The auxiliary flag counters reach their capacity before the size of the initial formed mesh could be reduced to zero

## Slide 19: Cycle Example
The mesh size is not reduced after an inversion
Faults pattern cannot be masked
 | SA-W |  | 
 |  |  | SA-W
0
1
1
0
VX
1
1
0
0
VY
invert
 |  |  | SA-W
0
2
2
0
VX
2
2
0
0
VY
Mesh Size cannot be reduced
Faults must form a cycle that is alternatively-stuck for RDIS to halt!

## Slide 20: Counters Capacity Example
A fault pattern cannot be masked due to counters capacity
Assume counters capacity is limited to 3.
SA-W |  |  | 
 | SA-W |  | 
 |  | SA-W | 
 |  |  | SA-W
1
1
1
1
VX
1
1
1
1
VY

## Slide 21: Counters Capacity Example
A fault pattern cannot be masked due to counters capacity
Assume counters capacity is limited to 3.
 | SA-W |  | 
 |  | SA-W | 
 |  |  | SA-W
2
2
2
1
VX
2
2
2
1
VY

## Slide 22: Counters Capacity Example
A fault pattern cannot be masked due to counters capacity
Assume counters capacity is limited to 3.
 | SA-W |  | 
 |  | SA-W | 
2
3
3
1
VX
2
3
3
1
VY

## Slide 23: Counters Capacity Example
A fault pattern cannot be masked due to counters capacity
Assume counters capacity is limited to 3.
2
3
3
1
VX
2
3
3
1
VY
Counters cannot be increased further

## Slide 24: Counters Capacity Example
A fault pattern cannot be masked due to counters capacity
Assume counters capacity is limited to 3.
Fault pattern must be an incomplete cycle that is alternatively-stuck
Faulty cell needed for cycle to be complete

## Slide 25: Evaluation
We rely on Monte-Carlo simulation to evaluate RDIS
We assume that all cells have equal probability of failure
We model an n * m memory block as bipartite graph with n + m nodes
A block is deemed defective when the faults form a cycle or an incomplete cycle
The defectiveness of a block is detected through a modification of the DFS algorithm.

## Slide 26: Related Work
SAFER[MICRO 10]: dynamically partitions a protected data block into a number of groups
  Each group contains at most one faulty cell
  Guaranties the recovery from lg n +1 faults, where n is the number of groups, and probabilistically from more faults.
ECP[ISCA 10]: provides a number of programmable correction entries to a protected data block
  A correction entry holds a pointer to faulty cell and a patch cell that replaced the faulty one
  The number of recovered faults is equal to the number of provided correction entries

## Slide 27: Fault Tolerance Capability
Chart: Avg. # of faults tolerated
| 512 bits | 1,024 bits | 2,048 bits | 4,096 bits | 8,192 bits
RDIS-3 | 21.0656 | 26.8032 | 35.33 | 45.46 | 60.16
RDIS-7 | 26.4 | 35.2355 | 47.51 | 63.46 | 85.7
RDIS-max | 26.85 | 36.34 | 49.93 | 69.29 | 94.32
Overhead (%)
Chart: 
| 512 bits | 1,024 bits | 2,048 bits | 4,096 bits | 8,192 bits
RDIS-3 | 18.7 | 12.5 | 9.3 | 6.2 | 4.6
RDIS-7 | 28.1 | 18.7 | 14 | 9.3 | 7
RDIS-max | 46.8 | 31.2 | 28.1 | 18.7 | 16.4
Block size

## Slide 28: Probability of Defectiveness
Chart: # of faults
Chart: # of faults
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49
RDIS-3 | 0 | 6e-06 | 3.2e-05 | 8e-05 | 0.000204 | 0.000418 | 0.000842 | 0.001504 | 0.002584 | 0.004535 | 0.007444 | 0.012339 | 0.019198 | 0.028984 | 0.042107 | 0.059682 | 0.081828 | 0.11029 | 0.14441 | 0.18465 | 0.23234 | 0.28636 | 0.34322 | 0.4068 | 0.47244 | 0.53915 | 0.60522 | 0.66898 | 0.72875 | 0.78435 | 0.832 | 0.87363 | 0.90809 | 0.93558 | 0.95594 | 0.9713 | 0.98166 | 0.9892 | 0.99396 | 0.9965 | 0.99822 | 0.99914 | 0.99958 | 0.99984 | 0.99468 | 0.9999 | 0.9999
RDIS-7 | 0 | 8e-06 | 3.8e-05 | 7.5e-05 | 0.000174 | 0.000377 | 0.000625 | 0.001152 | 0.001847 | 0.002762 | 0.003965 | 0.005702 | 0.007773 | 0.010514 | 0.013923 | 0.018203 | 0.023373 | 0.029334 | 0.036654 | 0.045966 | 0.05594 | 0.068461 | 0.082698 | 0.099405 | 0.11869 | 0.14092 | 0.1677 | 0.19759 | 0.23152 | 0.27146 | 0.31386 | 0.36072 | 0.41382 | 0.46915 | 0.52833 | 0.58688 | 0.64476 | 0.70482 | 0.76064 | 0.81018 | 0.85478 | 0.89314 | 0.92362 | 0.94716 | 0.96564 | 0.97872 | 0.98734
RDIS-max | 0 | 6e-06 | 3.2e-05 | 8e-05 | 0.000202 | 0.000395 | 0.000725 | 0.001182 | 0.001806 | 0.002804 | 0.00397 | 0.005737 | 0.007888 | 0.010634 | 0.013947 | 0.018132 | 0.023035 | 0.029228 | 0.036797 | 0.045317 | 0.055909 | 0.067863 | 0.082119 | 0.098557 | 0.11769 | 0.13849 | 0.16271 | 0.18998 | 0.22038 | 0.25381 | 0.29135 | 0.33135 | 0.3745 | 0.42079 | 0.46829 | 0.51924 | 0.57332 | 0.62392 | 0.67462 | 0.72534 | 0.77246 | 0.81416 | 0.85276 | 0.88694 | 0.91626 | 0.9394 | 0.95878 | 0.97356
Prob. having a defective pattern
1,024-bit block
2,048-bit block
RDIS-3
RDIS-7
RDIS-max
RDIS-3
RDIS-7
RDIS-max
Probability increases slowly with the relative increase in the number of faults!

## Slide 29: Aggregate Protection
Protect a large block through an aggregation of smaller sub-blocks
Declare defectiveness after the failure of the first sub-block
Chart: # of sub-blocks × sub-block size
| 1 × 8,192 bits | 2 × 4,096 bits | 4 × 2,048 bits | 8 × 1,024 bits | 16 × 512 bits
Avg. # of faults | 60.16 | 78.4432 | 104.43 | 136.537 | 181.974

## Slide 30: Aggregate Protection
Protect a large block through an aggregation of smaller sub-blocks
Declare defectiveness after the failure of the first sub-block
Chart: # of sub-blocks × sub-block size
| 1 × 8,192 bits | 2 × 4,096 bits | 4 × 2,048 bits | 8 × 1,024 bits | 16 × 512 bits
Avg. # of faults | 60.16 | 78.4432 | 104.43 | 136.537 | 181.974
Overhead | 4.6 | 6.2 | 9.3 | 12.5 | 18.7

## Slide 31: RDIS vs. SAFER
Chart: Avg. # of faults tolerated
| SAFER 64 | RDIS-3 | SAFER 128 | SAFER 64 | RDIS-3 | SAFER 128 | SAFER 128 | RDIS-3 | SAFER 256 | SAFER 128 | RDIS-3 | SAFER 256 | SAFER 256 | RDIS-3 | SAFER 512 | 512 bits | 1,024 bits | 2,048 bits | 4,096 bits | 8,192 bits
 | 12.41 | 21.0656 | 17.81 | 12.15 | 26.8032 | 16.85 | 16.46 | 35.33 | 23.05 | 16.27 | 45.4689 | 22.47 | 22.14 | 60.16 | 30.85
Chart: 
| SAFER 64 | RDIS-3 | SAFER 128 | SAFER 64 | RDIS-3 | SAFER 128 | SAFER 128 | RDIS-3 | SAFER 256 | SAFER 128 | RDIS-3 | SAFER 256 | SAFER 256 | RDIS-3 | SAFER 512 | 512 bits | 1,024 bits | 2,048 bits | 4,096 bits | 8,192 bits
 | 17.7 | 18.7 | 31 | 8.8 | 12.5 | 15.5 | 7.7 | 9.3 | 14.2 | 3.8 | 6.2 | 7.2 | 3.5 | 4.6 | 6.7
Overhead (%)
Block size
More Faults!
Less Overhead!

## Slide 32: RDIS vs. SAFER
Chart: # of faults
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
SAFER 64 | 0 | 0 | 0 | 0 | 0 | 0.10288 | 0.20882 | 0.31459 | 0.4168 | 0.51174 | 0.59835 | 0.67581 | 0.74294 | 0.80042 | 0.84774 | 0.88645 | 0.91696 | 0.94062 | 0.95839 | 0.97139 | 0.98072 | 0.98727 | 0.99184 | 0.99487 | 0.99679 | 0.99812 | 0.99889 | 0.99937 | 0.99965 | 0.99983 | 0.99991 | 0.99996 | 0.99998 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SAFER 128 | 0 | 0 | 0 | 0 | 0 | 0 | 0.055057 | 0.11391 | 0.17512 | 0.23763 | 0.301 | 0.36381 | 0.42536 | 0.48511 | 0.54196 | 0.59611 | 0.64666 | 0.69341 | 0.73593 | 0.77439 | 0.80897 | 0.83974 | 0.86654 | 0.89004 | 0.90996 | 0.92705 | 0.9415 | 0.95346 | 0.96336 | 0.97141 | 0.9779 | 0.98308 | 0.98699 | 0.99018 | 0.99267 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468 | 0.99468
RDIS-3 | 0 | 6e-06 | 3.2e-05 | 8e-05 | 0.000204 | 0.000418 | 0.000842 | 0.001504 | 0.002584 | 0.004535 | 0.007444 | 0.012339 | 0.019198 | 0.028984 | 0.042107 | 0.059682 | 0.081828 | 0.11029 | 0.14441 | 0.18465 | 0.23234 | 0.28636 | 0.34322 | 0.4068 | 0.47244 | 0.53915 | 0.60522 | 0.66898 | 0.72875 | 0.78435 | 0.832 | 0.87363 | 0.90809 | 0.93558 | 0.95594 | 0.9713 | 0.98166 | 0.9892 | 0.99396 | 0.9965 | 0.99822 | 0.99914 | 0.99958 | 0.99984 | 0.99468 | 0.9999 | 0.9999
Chart: # of faults
Prob. of failure
1,024-bit block
RDIS-3
SAFER 256
SAFER 128
2,048-bit block
RDIS-3
SAFER 128
SAFER 64

## Slide 33: RDIS Vs. ECP: Probability of Defectiveness
Chart: Prob. of failure
Chart: 
1,024-bit block
2,048-bit block
# of faults
# of faults
RDIS-3
RDIS-3
ECP 20
ECP 16

## Slide 34: Avg. # of Faults
Chart: Avg. # of faults tolerated
| 512-bit | 1024-bit | 2048-bit | 4096-bit | 8192-bit
RDIS-3PX | 21.18 | 27.2 | 35.09 | 45.51 | 59.6
ECP | 14 | 16 | 20 | 24 | 31
Chart: 
| 512 bits | 1,024 bits | 2,048 bits | 4,096 bits | 8,192 bits
RDIS-3PX | 26.7 | 16.5 | 11.6 | 7.3 | 5.3
ECP | 27.5 | 17.2 | 11.7 | 7.6 | 5.3
Overhead (%)
Block size
RDIS-3
ECP 16
ECP 20
ECP 24
ECP 31
RDIS-3PX
RDIS-3PX
RDIS-3
ECP 14
RDIS-3
RDIS-3
ECP 16
ECP 20
ECP 24
ECP 31
RDIS-3
RDIS-3
RDIS-3
ECP 14
RDIS-3
512 bits
1,024 bits
2,048 bits
4,096 bits
8,192 bits
512 bits
1,024 bits
2,048 bits
4,096 bits
8,192 bits
More Faults with less Overhead!

## Slide 35: Conclusion
Limited write endurance is a major weakness in PCM
Multi-bit error correction schemes are needed
We have presented RDIS as an error correction scheme that recursively identifies an invertible set containing all the stuck-at-wrong cell.
RDIS effectively masks a large number of stuck-at faults with an affordable overhead