## Slide 1: Power of One Bit: Increasing Error Correction Capability with Data Inversion
Rakan Maddah1, Sangyeun2,1 Cho and Rami Melhem1
1Computer Science Department, University of Pittsburgh
2Memory Solutions Lab, Memory Division, Samsung Electronics Co.
{rmaddah,cho,melhem}@cs.pitt.edu

## Slide 2: Introduction
DRAM and NAND flash are facing physical limitations putting their scalability into question
An alternative memory technology is under quest
Phase-Change Memory (PCM) is a promising emerging technology
  High scalability
  Low access latency
Initial measurements and assessments show that PCM competes favorably to both DRAM and NAND Flash

## Slide 3: PCM: The Basics
PCM cells are composed of Chalcogenide alloy ( Ge, Sb and Te)
PCM encode bits in different physical states through the application of varying levels of current to the phase change material
SET (Crystalline)
RESET (Amorphous)
time
Power

## Slide 4: PCM: The Challenges
Limited Endurance
  106 to 108 writes on average
  Early failure due to parametric variation in manufacturing
Slow Asymmetric Writes
  4x slower than reads
  Writing 0s is faster than 1s
Our focus is on the endurance problem

## Slide 5: PCM: Fault Model
A cell wears out when the heating element detaches from the chalcogenide material due to frequent expansions and contractions
A worn out cell gets permanently stuck
SA-1
SA-0
SA-1
SA-0
SA-1
SA-0

## Slide 6: Data-Dependent Errors
A Write on a memory block having a number of faults greater than the capability of the error correction code does not necessarily fail!
SA-1 | SA-1 |  |  | SA-0 | 
1 | 1 | 1 | 1 | 0 | 1
Physical state
Errors after write
1 | 0 | 1 | 1 | 0 | 1
Write Request
1 | 1 | 1 | 1 | 0 | 1
Errors after write
0 | 1 | 1 | 1 | 1 | 1
Write request
1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1
Write request
Errors after write

## Slide 7: Data-Dependent Errors
Example: With an ECC code of capability 2, only 1 write out of the 3 fails
A write fails only when the number of stuck-at wrong cells is above the capability of the ecc code
SA-1 | SA-1 |  |  | SA-0 | 
1 | 1 | 1 | 1 | 0 | 1
Physical state
Errors after write
1 | 0 | 1 | 1 | 0 | 1
Write Request
1 | 1 | 1 | 1 | 0 | 1
Errors after write
0 | 1 | 1 | 1 | 1 | 1
Write request
1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1
Write request
Errors after write
Can we exploit this fact to increase the ECC capability?

## Slide 8: Contribution: Data Inversion
After a write failure, Data Inversion reattempts a second write with the initial data inverted
  Polarity bit to flag inversion
Impact: stuck-at wrong (SA-W) cells exchange role with the stuck-at right (SA-R) cells
Consequence: only half of the faults in the data bits will manifest errors in the worst case
  Second write is successful if it brings the number of SA-W within the nominal capability of deployed error correction code
Achievement: Data Inversion can increase the number of faults before a block turns defective

## Slide 9: Data Inversion: Fault Tolerance Capability
The number of faults that can be tolerated depends on their distribution within the protected block
Data bits
Parity bits
Q Faults
R Faults
Block Defectiveness (t ECC capability)
Q + R >t Faults (Q SA-W + R SA-W in the worst case)
Data bits + Polarity bit
Parity bits
Q Faults
R Faults
Q/2 + R > t Faults (Q/2 SA-W + R SA-W in the worst case)

## Slide 10: Execution Flow: Write (ECC-1)
 |  |  |  | SA-1 |  |  |  |  |  |  |  | SA-0
Write pattern
Physical state
1st write
2nd write
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
Data inverted
auxiliary bits recomputed
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1

## Slide 11: Execution Flow: Read (ECC-1)
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
Physical state
Data decoded through ECC
Data read inverted
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
Can we do better?
Original data
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1

## Slide 12: Data Inversion: Unintegrated Protection
Un-integrate Polarity bit from the data bits
  Written infrequently
  Raw endurance should be enough
  Use other protection schemes e.g. TMR
Impact: after a write failure, invert the entire codeword
  Abolishes the need to recompute the auxiliary information
Achievement: doubles the number of faults that can be tolerated in a block before turning defective

## Slide 13: Unintegrated Protection: Fault Tolerance Capability
The number of faults that can be tolerated is doubled irrespective of the faults distribution within the protected block
Data bits + Parity bits
Parity bits
Q Faults
R Faults
Q/2 + R > t Faults (Q/2 SA-W + R SA-W in the worst case)
Block Defectiveness (t--ECC capability)
Data bits + Polarity bit
Q> 2t +1 Faults (t+1 SA-W and t+1 SA-R in the worst case)
Q Faults

## Slide 14: Execution Flow: Write (ECC-1)
SA-1 |  |  |  | SA-0 |  |  |  | SA-1 |  |  | 
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0
0
1
Physical state
1st write
2nd write with data inversion
Write pattern

## Slide 15: Execution Flow: Read (ECC-1)
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
Codeword read inverted
Data decoded through ECC
Physical state
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
Original codeword
1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1

## Slide 16: Integrated Vs. Unintegrated Protection
Chart: # of Faults
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
BCH-6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Block size: 512 bits
*BCH-6 (60 aux bits )

## Slide 17: Integrated Vs. Unintegrated Protection
Chart: # of Faults
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
BCH-6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
BCH-6 + DI + IP | 0 | 0 | 0 | 0 | 0 | 0 | 1.59e-07 | 3.0702e-05 | 0.0011107 | 0.015102 | 0.10025 | 0.3635 | 0.76328 | 1
Block size: 512 bits
*BCH-6 (60 aux bits )
*BCH-6 + Data Inversion +
Integrated Protection (60
aux bits + 1 polarity bit)

## Slide 18: Integrated Vs. Unintegrated Protection
Chart: # of Faults
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
BCH-6 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
BCH-6 + DI + IP | 0 | 0 | 0 | 0 | 0 | 0 | 1.59e-07 | 3.0702e-05 | 0.0011107 | 0.015102 | 0.10025 | 0.3635 | 0.76328 | 1
BCH-6 + DI + UP | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Block size: 512 bits
*BCH-6 (60 aux bits )
*BCH-6 + Data Inversion +
Integrated Protection (60
aux bits + 1 polarity bit)
*BCH-6 + Data Inversion +
unintegrated Protection (60
aux bits + 1 polarity bit)

## Slide 19: Evaluation
Monte Carlo Simulation
2000 Pages of memory
  512-bit cache line size for main memory protected by a BCH-6 code
  512-byte sector size for secondary storage protected by a BCH-20 code
Assign lifetime to cells based on a Gaussian distribution with a mean of 108 and stdev of
25 .106
A block is retired when the number of faults within it turns it defective
  In the case of unintegrated protection, a block is retired if the polarity bit wears out before the block turns defective

## Slide 20: Main Memory Lifetime
Lifetime of PCM main memory blocks achieved with BCH-6 and BCH-6 plus data inversion (DI) with integrated protection (IP) and un-integrated protection (UP).
21.1%
34.5%

## Slide 21: Secondary Storage Lifetime
Chart: Writes per Block (Million)
Lifetime of PCM storage blocks achieved with BCH-20 and BCH-20 plus data inversion (DI) with integrated protection (IP) and un integrated protection (UP). This experiment assumed that 20% of spare storage capacity was provided.
25.2%
18.1%

## Slide 22: Performance Overhead
 | Data Inversion with Integrated Protection |  | Data Inversion with Un-Integrated Protection | 
 | Avg. % of extra writes before nominal capability is exceeded | Avg. % of extra writes after nominal capability is exceeded | Avg. % of extra writes before nominal capability is exceeded | Avg. % of extra writes after nominal capability is exceeded
512 bits | 0% | 4.9% | 0% | 13.1%
4096 bits | 0% | 6.4% | 0% | 8.9%
Performance evaluation in terms of extra write operations required by data inversion to complete write requests successfully after the number of faults exceeds the nominal capability of the error correction code.

## Slide 23: Conclusion
Data Inversion is a simple yet powerful technique to increase the number of faults that an error correction code can tolerate
Two variations:
  Integrated Protection: Block defectiveness depends on the distribution of faults within the block
  Unintegrated Protection: Doubles the number of faults that can be tolerated
Data inversion extends the lifetime significantly while incurring a low performance overhead and a marginal physical overhead of one additional bit

## Slide 24: Thank You!!
Contact info:
  Rakan Maddah: www.cs.pitt.edu/~rmaddah
  Sangyeun Cho: www.cs.pitt.edu/~cho
  Rami Melhem: www.cs.pitt.edu/~melhem