## Slide 1: Scalable Multi-Cache Simulation Using GPUs
Michael Moeng
Sangyeun Cho
Rami Melhem
University of Pittsburgh

## Slide 2: Background
Architects simulating more cores
  Increasing simulation times
Cannot keep doing single-threaded simulations if we want to see results in a reasonable time frame
Host Machine
Simulates
Target Machine
Notes: Motivate fast simulation in context of CMPs
Motivate study of memory subsystem or uncore

## Slide 3: Parallel Simulation Overview
A number of people have begun researching multithreaded simulation
Multithreaded simulations have some key limitations
  Many fewer host cores than the cores in a target machine
  Slow communication between threads
Graphics processors have high fine-grained parallelism
  Many more cores
  Cheap communication within ‘blocks’ (software unit)
We propose using GPUs to accelerate timing simulation
CPU acts as the functional feeder
Notes: Parallel simulation
Graphics processing – rapid growth of features/capabilities

## Slide 4: Contributions
Introduce GPUs as a tool for architectural timing simulation
Implement a proof-of-concept multi-cache simulator
Study strengths and weaknesses of GPU-based timing simulation
Notes: Our contributions

## Slide 5: Outline
GPU programming with CUDA
Multi-cache simulation using CUDA
Performance Results vs CPU
  Impact of Thread Interaction
  Optimizations
Conclusions
Notes: Outline

## Slide 6: CUDA Dataflow
Host (CPU)
Main Memory
Device (GPU)
SIMD Processors
Graphics Memory
PCIe Bus
Notes: CUDA programming. Basic transfer ->compute

## Slide 7: Dataflow – Concurrent CPU/GPU
Host (CPU)
Main Memory
Device (GPU)
SIMD Processors
Graphics Memory
PCIe Bus
Notes: Simultaneous CPU compute

## Slide 8: Dataflow – Concurrent Kernels
Host (CPU)
Main Memory
Device (GPU)
SIMD Processors
Graphics Memory
PCIe Bus
Notes: Multiple kernels

## Slide 9: GPU-driven Cache Simulation
Trace-driven Simulation
Host (CPU)
Device (GPU)
L1 kernel
L2 kernel
Trace Data
L1 Misses
Statistics
Trace Data
Notes: Transfer a chunk of trace data over to GPU

## Slide 10: GPU-driven Cache Simulation
Each cache way is simulated by a thread
  Parallel address lookup
  Communicate via fast shared memory
Ways from 4 caches form a block
  With 16-way caches, 64 threads per block
Cache state (tags+metadata) stored in global memory – rely on caching for fast access
Experimented with tree-based reduction
  No performance improvement (small tree)

## Slide 11: Block-to-Block Interactions
Within a block, we can call a cheap barrier and there is no inaccuracy
Shared L2
  Upon miss, L1 threads determine L2 home tile
  Atomically add miss to global memory buffer for L2 to process
Write Invalidations
  Upon write, L1 thread checks global memory for tag state of other L1 threads
  Atomically invalidate matching lines in global memory
Notes: Handling Thread Interaction

## Slide 12: Evaluation
Feed traces of memory accesses to simulated cache hierarchy
  Mix of PARSEC benchmarks
L1/L2 cache hierarchy with private/shared L2
GeForce GTS 450 – 192 cores (low-mid range)
  Fermi GPU – caching, simultaneous kernels
  Newer NVIDIA GPUs range from 100-500 cores

## Slide 13: Private L2
Chart: Workload
| A | B | C | D | E | F
CPU 32 | 1 | 1 | 1 | 1 | 1 | 1
CPU 64 | 2.1214 | 2.3227 | 2.3918 | 2.0394 | 2.2813 | 2.0876
CPU 96 | 3.6149 | 3.1711 | 3.6537 | 3.2559 | 3.5358 | 3.3162
GPU 32 | 0.4878 | 0.45433 | 0.48335 | 0.49329 | 0.56743 | 0.59575
GPU 64 | 0.52251 | 0.48671 | 0.51696 | 0.5234 | 0.60147 | 0.63801
GPU 96 | 0.7677 | 0.70989 | 0.76929 | 0.55762 | 0.65472 | 0.6785
Linear CPU simulation scaling
GPU sees 13-60% slowdown from 32 to 96 caches
Multithreaded
Notes: GPU slowdown average 35%

## Slide 14: Shared L2
Chart: Workload
| A | B | C | D | E | F
CPU 32 | 1 | 1 | 1 | 1 | 1 | 1
CPU 64 | 2.0878 | 2.0858 | 2.1573 | 2.0647 | 2.0654 | 2.0334
CPU 96 | 3.6041 | 3.3636 | 3.5428 | 3.3274 | 3.3331 | 3.3023
GPU 32 | 0.85718 | 1.3951 | 0.809 | 1.9033 | 1.4246 | 1.35
GPU 64 | 0.89874 | 2.1043 | 0.85064 | 3.2535 | 2.1338 | 2.0385
GPU 96 | 0.93896 | 1.4656 | 0.88322 | 1.9887 | 1.5196 | 1.4222
Unbalanced traffic load to a few tiles
Largely serialized
Multithreaded

## Slide 15: Inaccuracy from Thread Interaction
CUDA currently has little support for synchronization between blocks
Without synchronization support, inter-thread communication is subject to error:
  Shared L2 caches – miss rate
  Write invalidations – invalidation count

## Slide 16: Controlling Error
Only way to synchronize blocks is in between kernel invocations
  Number of trace items processed by each kernel invocation controls error
  Similar techniques used in parallel CPU simulation
There is a performance and error tradeoff with varying trace chunk size

## Slide 17: Invalidation – Performance vs Error
Chart: Trace Chunk Size
| 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
Error | 0.011009 | 0.021621 | 0.03515 | 0.05048 | 0.06402 | 0.079441 | 0.090143 | 0.097958 | 0.10959
Performance | 0.11896 | 0.23197 | 0.43891 | 0.7008 | 0.87347 | 0.93248 | 0.97537 | 0.99105 | 1
CPU-only | 0.32411 | 0.32411 | 0.32411 | 0.32411 | 0.32411 | 0.32411 | 0.32411 | 0.32411 | 0.32411

## Slide 18: Shared L2 – Miss Rate Error
Chart: Workload
| A | B | C | D | E | F
32 | 0 | 0.0011 | 0 | 0.0019 | 0.0007 | 0.0001
64 | 0 | 0.0001 | 0 | 0.001 | 0.0008 | 0.0003
96 | 0 | 0.0004 | 0 | 0.0063 | 0.0023 | 0
Largely serialized execution minimizes error
Notes: Shared miss rates low – maximum error

## Slide 19: Concurrent Execution
Transfer memory while executing kernels
Run L1 kernel concurrently with L2 kernel
Trace IO
L1 Kernel
L2 Kernel
Trace IO
L1 Kernel
L2 Kernel
Trace IO
L1 Kernel
L2 Kernel

## Slide 20: Concurrent Execution Speedup
Chart: Simulated Cache Tiles
| 32 | 64 | 96
L1 | 0.2513 | 0.46501 | 0.70113
Private | 0.5649 | 0.7529 | 0.63626
Shared | 0.068032 | 0.10426 | 0.22741
Greater benefit when more data is transferred
Benefits end when GPU is fully utilized
Load imbalance among L2 slices
Cache
Model
From better utilization of GPU
From parallel memory transfer and computation

## Slide 21: CUDA Block Mapping
For maximum throughput, CUDA requires a balance between number of blocks and threads per block
  Each block can support many more threads than the number of ways in each cache
We map 4 caches to each block for maximum throughput
Also study tradeoff from fewer caches per block

## Slide 22: Block Mapping - Scaling
Chart: Simulated Cache Tiles
| 16 | 32 | 48 | 64 | 80 | 96
1 | 1 | 1.03 | 1.8885 | 2.0139 | 2.7954 | 2.9901
2 | 1.4159 | 1.4796 | 1.5279 | 1.5673 | 2.7181 | 2.8659
4 | 1.7972 | 1.8665 | 1.9224 | 1.9653 | 2.0061 | 2.0479
Saturated at 32 tiles
Saturated at 64 tiles
More Caches per Block
Higher Throughput
Fewer Caches per Block
Lower Latency
Notes: Maybe better words than latency+throughput?

## Slide 23: Conclusions
Even with a low-end GPU, we can simulate more and more caches with very small slowdown
With a GPU co-processor we can leverage both CPU and GPU processor time
Crucial that we balance the load between blocks

## Slide 24: Future Work
Better load balance (adaptive mapping)
More detailed timing model
Comparisons against multi-threaded simulation
Studies with higher-capacity GPUs