## Slide 1: AN ANALYTICAL MODEL TO STUDY OPTIMAL AREA BREAKDOWN BETWEEN CORES AND CACHES IN A CHIP MULTIPROCESSOR
Taecheol Oh, Hyunjin Lee, Kiyeon Lee
and Sangyeun Cho

## Slide 2: Processor design trends
Clock rate, core size, core performance growth have ended
UC Berkeley 2009
Transistors(000)
Clock Speed (MHZ)
Power (W)
Perf/Clock
How many cores shall we integrate on a chip?
(or how much cache capacity)
Notes: Moore’s law reinterpreted
  Number of cores per chip will double every two years
  Clock speed will not increase (possibly decrease)
  The chip size will remain constant

## Slide 3: How to exploit the finite chip area
A key design issue for chip multiprocessors
The most dominant area-consuming components in a CMP are cores and caches
  Too few cores :
    System throughput will be limited by the number of threads
  Too small cache capacity :
    System may perform poorly
We presented a first order analytical model to study the trade-off of the core count and the cache capacity in a CMP under a finite die area constraint

## Slide 4: Talk roadmap
Unit area model
Throughput model
Multicore processor with L2 cache
  Private L2
  Shared L2
    UCA (Uniform Cache Architecture)
    NUCA (Non-Uniform Cache Architecture)
    Hybrid
Multicore processor with L2 and shared L3 cache
  Private L2
  Shared L2
Case study

## Slide 5: Unit area model
Given die area A, core count N, core area Acore and cache area AL2 , AL3
Define A1 as the chip area equivalent to a 1MB cache area
c1
Area for Caches(L2 / L3)
cN
Area for Cores
  Where m and c are design parameters
≥
c2
A1

## Slide 6: Throughput model
IPC as the metric to report system throughput
  To compute IPC, we obtain CPI of individual processors
    A processor’s “ideal” CPI can be obtained with an infinite cache size
    mpi : the number of misses per inst. for the cache size,
      The square root rule of thumb is used to define mpi. [Bowman et al. 07]
    mpM : the average number of cycles needed to access memory and handle an L2 cache miss

## Slide 7: Modeling L2 cache
Core 0
L1
L2
Core 0
L1
L2
• • • • • •
Core 0
L1
L2
Core 0
L1
• • • • • •

## Slide 8: Modeling private L2 cache
Private L2 cache offers low access latency, but may suffer from many cache misses
  CPIpr is the CPI with an infinite private L2 cache (CPIideal)
  Per core private cache area and size

## Slide 9: Modeling shared L2 cache
Shared L2 cache shows effective cache capacity than the private cache
  CPIsh is the CPI with an infinite shared L2 cache (CPIideal)
  SL2sh is likely larger than SL2p
    There are cache blocks being shared by multiple cores
    A cache block is shared by Nsh cores on average

## Slide 10: Modeling shared L2 cache
UCA (Uniform Cache Architecture)
  Assuming the bus architecture
  Contention factor
NUCA (Non Uniform Cache Architecture)
  Assuming the switched 2D mesh network
  B/W penalty factor, average hop distance, single-hop traverse latency
  Network traversal factor
Hybrid
  Cache expansion factor σ

## Slide 11: Modeling on-chip L3 cache
Parameter α to divide the available cache area between L2 and L3 caches
Core 0
L1
L2
Core 0
L1
L2
• • • • • •
Core 0
L1
L2
Core 0
L1
• • • • • •
L3
L3

## Slide 12: Modeling private L2 + shared L3
Split the finite cache CPI into private L2 and L3 components
Private L2 cache size and shared L3 cache size

## Slide 13: Modeling shared L2 + shared L3
Split the finite cache CPI into shared L2 and L3 components
UCA (Uniform cache Architecture)
  Contention factor
NUCA (Non uniform cache Architecture)
  Network traversal factor
Hybrid
  Cache expansion factor σ

## Slide 14: Validation
Comparing the IPC of the proposed model and the simulation (NUCA)
  TPTS simulator [Cho et al. 08]
    Models a multicore processor chip with in-order cores
  Multi threaded workload
    Running multiple copies of single program
  Benchmark
    SPECK2k CPU suite
  Good agreement with the simulation before a “breakdown point” (48 cores)
Notes: Around 20 mb

## Slide 15: Case study
Employ a hypothetical benchmark
  To clearly reveal the properties of different cache organizations and the capability of our model
Select base parameters
  Obtained experimentally from the SPEC2k CPU benchmark suite
Change the number of processor cores
Show how that affects the throughput
  Chip area, core size, and the 1 MB cache area
  At most 68 cores (with no caches) and 86 MB cache capacity (with no cores)

## Slide 16: Performances of different cache design
Performance of different cache organization peaks at different core counts.
Hybrid scheme exhibits the best performance
Shared scheme can exploit more cores
The throughputs drop quickly as more cores are added
  The performance benefit of adding more core is quickly offset by the increase in cache misses

## Slide 17: Effect of on-chip L3 cache (α= 0.2)
The private and hybrid schemes outperform the shared schemes
The relatively high miss rate of the private scheme is compensated by the on-chip L3 cache (low access latency to private L2)

## Slide 18: Effect of off-chip L3 cache
With the off-chip L3 scheme favors over without off-chip L3
The private and the hybrid schemes benefit from the off-chip L3 cache the most
Notes: Off-chip 128 MB

## Slide 19: Conclusions
Presented a first order analytical model to study the trade-off between the core count and the cache capacity
Differentiated shared, private, and hybrid cache organizations
The results show that different cache organizations have different optimal core and cache area breakdown points
With L3 cache, the private and the hybrid schemes produce more performance than the shared scheme, and more cores are allowed to be integrated in the same chip area (e.g. Intel Nehalem, AMD Barcelona)

## Slide 20: Question