## Slide 1: An Analytical Performance Model for Co-Management of Last-Level Cache and Bandwidth Sharing
Taecheol Oh, Kiyeon Lee, and Sangyeun Cho
Computer Science Department
University of Pittsburgh

## Slide 2: Chip Multiprocessor (CMP) design is difficult
Performance depends on the efficient management of shared resources
Modeling CMP performance is difficult
  The use of simulation is limited

## Slide 3: Shared resources in CMP
Shared cache
  Unrestricted sharing can be harmful
  Cache partitioning
Off-chip memory bandwidth
  BW capacity grows slowly
  Off-chip BW allocation
App 1
Cache
App 2
Bandwidth
?
?
?
Any interaction between the two shared resource allocations?

## Slide 4: Co-management of shared resources
Assumptions
  Cache and off-chip bandwidth are the key shared resources in CMP
  Resources can be partitioned among threads
Hypothesis
  An optimal strategy requires a coordinated management of shared resources
cache
Off-chip bandwidth
On-Chip
Off-Chip

## Slide 5: Contributions
Combined two (static) partitioning problems of shared resources for out-of-order processors
Developed a hybrid analytical model
  Predicts the effect of limited off-chip bandwidth on performance
  Explores the effect of coordinated management of shared L2 cache and the off-chip bandwidth

## Slide 6: OUTLINE
Motivation/contributions
Analytical model
Validation/Case studies
Conclusions

## Slide 7: Machine model
Out-of-order processor cores
L2 cache and the off-chip bandwidth are shared by all cores

## Slide 8: Base model
CPIideal
  CPI with an infinite L2 cache
CPI penaltyfinite cache
  CPI penalty caused by finite L2 cache size
CPI penaltyqueuing delay
  CPI penalty caused by limited off-chip bandwidth
CPI = CPIideal + CPI penaltyfinite cache + CPI penaltyqueuing delay

## Slide 9: Base model
CPI penaltyfinte cache
CPI = CPIideal + CPI penaltyfinite cache + CPI penaltyqueuing delay
    - C0: a reference cache size
    - α:power law factor for cache size

## Slide 10: Base model
CPI penaltyfinte cache
  The effect of overlapped independent misses [Karkhanis and Smith`04]
CPI = CPIideal + CPI penaltyfinite cache + CPI penaltyqueuing delay
    f(i): probability of i misses in a given ROB size
    MLPeffect=

## Slide 11: Base model
Why extra queuing delay?
  Extra delays due to finite off-chip bandwidth
CPI penaltyqueuing delay
CPI = CPIideal + CPI penaltyfinite cache + CPI penaltyqueuing delay

## Slide 12: Modeling extra queuing delay
Simplified off-chip memory model
  Off-chip memory requests are served by a simple memory controller
    m identical processing interfaces, “slots”
    A single buffer
    FCFS
Use a statistical event driven queuing delay (latqueue) calculator
Waiting buffer
Identical slots

## Slide 13: Modeling extra queuing delay
Input: ‘miss-inter-cycle’ histogram
  A detailed account of how dense a thread would generate off-chip bandwidth accesses throughout the execution

## Slide 14: Modeling extra queuing delay
The queuing delay decreases with a power law of off-chip bandwidth capacity (slot count)
    - latqueue0 is a baseline extra delay
    slot : slot count
    β: power law factor for queuing delay

## Slide 15: Shared resource co-management model
CPI = CPIideal +CPI penaltyfinite cache + CPI penaltyqueuing delay

## Slide 16: Bandwidth formulation
Memory bandwidth (B/s) = Data transfer size (B) / Execution time
  Data transfer size = Cache misses x Block size (BS)
  = IC x MPI x BS
  Execution time (T) =
The bandwidth requirement (BWr) for a thread
  The effect of off-chip bandwidth limitation
    (latM: mem. access lat., F: clock freq.)
    (IC: instruction count, MPI: # misses/instruction)
    (BWS: system bandwidth)

## Slide 17: OUTLINE
Motivation/contributions
Analytical model
Validation/Case studies
Conclusions

## Slide 18: Setup
Use Zesto [Loh et al. `09] to verify our analytical model
  Assumed dual core CMP
Workload: a set of benchmarks from SPEC CPU 2006

## Slide 19: Accuracy (cache/BW allocation)
Chart: Normalized CPI
| 128KB | 256KB | 512KB | 1MB | 2MB | 4MB
Sim | 1.441 | 1.2162 | 1.1408 | 1.1098 | 1.046 | 1
Anal | 1.6821 | 1.3989 | 1.2222 | 1.1118 | 1.043 | 1
Chart: Normalized CPI
| 2 slots | 4 slots | 6 slots | 8 slots | 10 slots
Sim | 1.0492 | 1.0057 | 1.0013 | 1.0003 | 1
Anal | 1.0361 | 1.0038 | 1.0004 | 1 | 1
    astar
Cache capacity has a larger impact
    Cache capacity
    Off-chip bandwidth

## Slide 20: Accuracy (cache/slot allocation)
Chart: Normalized CPI
| 128KB | 256KB | 512KB | 1MB | 2MB | 4MB
Sim | 1.0088 | 1.006 | 1.0058 | 1.0058 | 1.0005 | 1
Anal | 1.0216 | 1.0171 | 1.0127 | 1.0084 | 1.0041 | 1
Chart: Normalized CPI
| 2 slots | 4 slots | 6 slots | 8 slots | 10 slots
Sim | 1.3901 | 1.0991 | 1.0375 | 1.0054 | 1
Anal | 1.3851 | 1.1132 | 1.0366 | 1.01 | 1
    bwaves
Off-chip bandwidth has a larger impact
    Cache capacity
    Off-chip bandwidth

## Slide 21: Accuracy (cache/slot allocation)
Cache capacity allocation:
  4.8 % and 3.9 % error (arithmetic, geometric mean)
Off-chip bandwidth allocation
  6.0 % and 2.4 % error (arithmetic, geometric mean)
Chart: Normalized CPI
| 128KB | 256KB | 512KB | 1MB | 2MB | 4MB
Sim | 1.0807 | 1.0447 | 1.0315 | 1.0305 | 1.0272 | 1
Anal | 1.1267 | 1.0766 | 1.044 | 1.0228 | 1.009 | 1
Chart: Normalized CPI
| 2 slots | 4 slots | 6 slots | 8 slots | 10 slots
Sim | 1.5579 | 1.1811 | 1.0428 | 1.0121 | 1
Anal | 1.7907 | 1.2297 | 1.0619 | 1.0135 | 1
    cactusADM
Both cache capacity and off-chip bandwidth have large impacts
    Cache capacity
    Off-chip bandwidth

## Slide 22: Case study
Dual core CMP environment for the simplicity of the system
Used Gnuplot 3D
Examined different resource allocations for two threads A and B
  L2 cache size
    from 128 KB to 4 MB
  Slot count
    from 1 to 4 (1.6 GB/S peak bandwidth)

## Slide 23: System optimization objectives
Throughput
  The combined throughput of all the co-scheduled threads
Fairness
  Weighted speedup metric
  How uniformly the threads slowdown due to resources sharing
Harmonic mean of normalized IPC
  Balanced metric of both fairness and performance

## Slide 24: Throughput
The summation of two thread’s IPC
(i)
(ii)
IPC

## Slide 25: Fairness
The summation of weighted speedup of each thread
WS
(ii)
(iii)
(i)

## Slide 26: Harmonic mean of normalized IPC
The sum. of harmonic mean of normalized IPC of each thread
(i)
HMIPC

## Slide 27: OUTLINE
Motivation/contributions
Analytical model
Validation/case studies
Conclusions

## Slide 28: Conclusions
Co-management of the cache capacity and off-chip bandwidth allocation is important for optimal design of CMP
Different system optimization objectives change optimal design points
Proposed an analytical model to easily compare the impact of different resource allocation decisions on the system performance

## Slide 29
Thank you !